AN355

BRAKE REBUILD PART #2

Brake Hoses and Cylinders

I just replaced the brake hoses on my 95 front calipers and following Jan '89 NINES, I have the following revelations:

As a result of brake drag due to faulty brake hoses, I tackled replacement of the caliper hoses and came up with the following:

1. New replacements hoses from a SAAB dealer are expensive, about    $27.00 each.

2. Same above hoses do not last. The hole (3/32") is too small and    collapses easily.

For these reasons, I decided on an alternate solution. I used MGB hoses which are about 3" longer (position the hoses with a loop vertical and slightly forward to miss stationary and moving parts), but otherwise the same as SAAB hoses as fittings go. The advantages to the MGB hoses are that they're only $11.05 each and are available from Moss Motors (7200 Hollister Ave., Goleta, Ca. 93116. Toll free phone number: US 1-800-235-6596 or in Calif only 1-800-322-6985) or any brake parts supply house. The part numbers are:

Hose, front caliper    180-985

Hose, rear cylinder    180-835

You might also use MGB rear brake cylinders on 95 and 96's. They are reasonably priced and available from Moss Motors also. there are two differences however. First the MGB cylinders have a larger bores. This alters the braking pressure as to front/rear ratios. The difference isn't very noticeable, unless you're a purist or  high performance SAABer. Second, An opposite-hand hole has to be drilled into the backing plate to accommodate the MGB brake cylinder locating pin.