AN356

BRAKE REBUILDING PART #3

If your bleeding heart do-it-yourself, here's how to build your own brake bleeding system:

A Coleman Stove is frequently found at swap meets. Should you find one, the hand-pumped pressure reservoir makes up the heart of your home built system. You'll spot the red canister which is all you'll need. The pump should be oiled at the hole at the base of its shaft.

Unscrew the tip off the tube extending from the canister and remove the inner coiled wire. Discard these. With a hacksaw, cut off all but about an inch of said tube. To do this, install a 1-1/2 foot length of suitable hose (I used 3/8" clear nylon plastic tubing). Secure this to the canister tube with a hose clamp.

Obtain extra master cylinder caps for the system you intend to bleed. A small white plastic cap suffices the clutch master cylinder, and a larger black plastic cap serves the brake master cylinder. You'll find such caps at foreign car boneyards, or on discarded master cylinders. spray the caps clean with brake parts cleaner.

Drill said caps to take a 2" length of plastic tubing that will fit into the 3/8" tubing. (The red tubing found on early SAAB clutch systems works nicely). These short tube stubs may then be glued into the master cylinder caps (extending about 1/4" below the caps). Use "PVC adhesive", the type used for white plumbing, or IPS Weld-On 1807 as found at a plastic supply house. These glues are actually solvents which chemically fuse-weld the stubs tubes to the caps.

The larger black cap will require additional support. Cut triangular right angled pieces from scrap plastic, 1/4" thick, about an inch high, and glue these supports to the stub tube around the top of the cap. Install the cap washer.

Clamp either of the above cap assemblies, as requires for the master cylinder to pressurize, to the long tube with a hose clamp. Fill the master cylinder with brake fluid, Screw the bleed system cap onto the master cylinder.

Pump up the tank (about 16 strokes), then open the valve on the tank and the master cylinder is pressurized. (Another way would be to use a bicycle pump and a tire valve with plastic tubing attached).

Proceed to open the various brake cylinder bleed screws, starting at the rear. Replenish the master before it runs out, and

AN356

pressurize the system as required during the bleeding process, until the fluid flows clean and steadily and free of air bubbles.