AN358

STILLBORN SONETT

In the early 1960s, sports cars were selling well.  It was the era of the Bugeye Sprite and 3000 by Austin Healey, the Triumph TR-3, the MGA, the XK-150.  From Italy there was the Alfa Fiulietta and the Fiat 1200; from Germany the Porsche 356.  1960 saw the introduction of the MG Midget, the Triumph TR-4, the Jaguar XK-E and the Volvo P1800; a year later the MGB and Triumph Spitfire joined the sports car crowd.

Walter Kern was a sports car enthusiast who spent some of his time in competition on the race tracks of New England.  He started with an MG-TD, then moved up to a Siata, an Italian-made car designed for a Crosley engine.  Kern took delivery of the Siata without a powerplant and adapted it to take a Fiat 1100cc engine.  After a bit of tuning and building up, the Siata was a competitive race car.

From there Kern moved on to a Porsche 356, but got rid of it after its' two quart sump ran low on oil and broke the crankshaft.  He bought another Siata and raced it twice, only to have it, too, lose its engine bearings.

By 1958, Kern had enough of sports cars that suffered engine failure when the oil sloshed to one side of the sump while cornering.  About that time, SAAB started importing 93s through Himgham, Massachusetts, and Kern noticed the little sedans as he drove past the unloading dock every day.  He looked up the local SAAB dealer and found out about the two-stroke engine and front-wheel drive.  Here was a solution to engine failures since the engine's lubrication was added with the gas.  It also had the advantage of putting out lots of horsepower for its weight and size.  And according to his way of thinking, front-wheel-drive should be an advantage on the race track since it pulled the car through corners rather than pushed.  But he needed a sports car to wrap around the drivetrain.

Kern, an MIT grad in nuclear physics, and Jack Suomala, who worked at the MIT Instrumentation Lab, discussed the idea on the train on the way home to the South Shore.  Suomala had been a classmate of Ralph Millet, then president of SAAB Motors of America.  He arranged an introduction betweens the two and Millet became convinced that the idea had promise.  So much promise that Millet opened the parts warehouse to whatever Kern needed.

It was then on to the  chassis design stage.  Kern had some help in this from Al Conrod of Itek Corp., who wrote the dynamic design equations, and Suomala, who programmed them into MIT's giant IBM computer.  Utilizing the computer, Kern was able to design a lightweight yet strong chassis using aluminum tubing.  Remember

AN358

this was thirty years ago, long before computer aided design (CAD), when computer programming was still in its infancy.

For ease of construction, the first chassis was built of steel.  At Suomala's suggestion the center of gravity and the center of lateral resistance were at the same point.  The idea was there would be no net forces on the car once in a corner, i.e. you could let go of the steering wheel and the car would continue to circle.  The computer projection showed the car could take a 40-foot radius turn at 40 mph.  Since the tightest corner on any known racetrack was a 60-foot radius, cornering was not expected to be a problem.

The completed chassis was first tested at Thompson Raceway in Connecticut in January, 1960.  It had been fitted with a stock 37 hp SAAB three-cylinder mounted normally, but the radiator was moved to the rear of the car.  It also used stock suspension parts from the SAAB 93.  The car had no body at this point, and Kern sat on a three inch cushion for the initial test session.

The temperature was well below freezing and snow had to be plowed form the track before the tests could begin.  After a few practice laps, the Quantum turned the 1.5 mile course at 2:00 minutes flat, equaling the H-modified track record first time out.

A hand-built aluminum body was fitted to the car, and on May 21, 1960, the Quantum/SAAB ran its first race with Joe Dodge behind the wheel.  The race tool place in the rain, and Dodge was the winner, beating two Ferraris and a Maserati that were dominating racing in the area at the time.  In about a dozen races that season, Dodge and the Quantum were never beaten in the class, and often finished ahead of winners in larger engine classes.

SAAB was interested in selling this neutral-handling sports car, so the Quantum Corporation was formed and a second chassis was built.  This one was made from aluminum tubing.  For better weight distribution, the drivetrain was turned around, engine behind the transmission, like the SAAB Sonett I of the mid-'50s.  The engine was made to run in the opposite direction, an easy thing to do with a two stroke.  A reverse distributor and starter were built, and the water pump impeller was changed.

The frame underwent non-destructive testing by an independent lab in Connecticut.  The right front of the frame was secured to the floor and the left front was raised until the stress lacquer fractured.  All the joints failed at the same time!

Chester Wiley, then vice-president of Atkins & Merrill, built the fiberglass body for the second chassis in his garage.  At SAAB's request, the body was made to look similar to the E-type Jaguar.  This car, the only white Quantum, was shown at the New York Auto

AN358

Show in 1962.  It was pushed to its place on the display stand as it could not be driven.  After the NY debut, Wiley made molds for future Quantums from the hand-laid body of the show car.  It was destroyed in the process.

The next Quantum sports car had a chassis built of mild steel.  Again, this was a concession to SAAB, who wanted to keep costs down and assembly simple.  Much of this car was assembled only for looks, as the windshield wipers are only a mockup, and there is no heater.  The headlight assemblies came from a bull-nose SAAB and have no protective buckets, meaning the back sides of the lights are open to the front tires.  This car is now owned by Bud Clarke of J & B Imports in California.

The final Quantum sports car also had a steel chassis, and looks more like a production car would.  The fit and finish are better, the trunk is finished off, and components such as the upholstery and shifter are more like the sports cars of their day and less like a backyard special.  The headlight buckets are from Lucas and the windshield wipers work.  It is also at J & B Imports, owned by Jay Arruda.

Ralph Millet was still excited about the prospect of a SAAB powered sports car built in the United States and expressed his enthusiasm to Rolf Mellde in a letter when the Quantum was shipped to Trollhattan.  A marketing study was undertaken which also indicated the Quantum/SAAB sports car was needed for the U.S. market.  But the researchers apparently based their conclusions more on what SAAB Motors, Inc. wanted to hear than on actual results.  Most of the sports car owners surveyed said the car needed a proper floor shifter, not a column shift.  The two-stroke engine was also a negative point with the sports car crowd.

By comparing the Quantum with the Ford Mustang and Plymouth Valiant instead of more likely competitors such as the MGB, the researchers indicated that SAAB dealers should be able to sell a thousand care the first year, and 5,000 annually after five years.  The study concluded, "Make sure it comes into production as quickly as possible!"

SAAB engineers were not very impressed with the Quantum that was sent to Sweden.  They complained about the body, which leaked in rain; they complained the instruments were unreadable; they complained that exhaust odors got into the passenger compartment.  Kern's reaction was that he and his associated were new to the car building game and shortcomings were to be expected, and could be corrected.

On the test track, the Quantum was compared with the Triumph Spitfire.  With the standard 850cc engine, the Quantum was no match

AN358

for the Spitfire, but once the Sport engine was fitted, the Quantum fared much better.  Nevertheless, the testing department panned the Quantum:

"As a touring car, the Quantum is far less attractive the Saab Sport and the Triumph Spitfire.  The noise level is excessive and it offers poor protection against winds and rain.  It is difficult to enter and get out of, has very little luggage space, has a less-than-elegant interior, is less comfortable in all respects and the controls are less functional (e.g. gear shift and clutch pedal)."

Apparently the management at SAAB in Sweden felt they could do better, as it was about this time that they wrote down specifications for a possible SAAB sports car.  This led to the development of the Sonett II which went into production less than three years later.

Saab eventually bought out the Quantum Corporation, but never really did anything with it.  Or did they?

Though the Karlstron prototype was selected to become the Sonett II in 1965, some of the chassis ideas from the Quantum were apparently carried over the Sonett had some understeer desinged into it rather than the neutral handling of the Quantum, to give it a feel more like other sports cars of the era.

AN358

When the Quantum went on display at the New York Auto Show, the following news releases gave details on the potential of the SAAB powered sports car.

PRESS INFORMATION

QUANTUM SAAB

Introduction

The Quantum SAAB you see here at the New York Auto-

mobile Show is the result of four years of engineering

and design data gathered by Mr. Walter Kern.  Mr. Kern

originally conceived the idea of a front-wheel drive,

small, light-weight, safe, two-passenger sports roadster.

It was natural for Mr. Kern to pick the basic SAAB power

plant and running gear because of his past knowledge of

SAAB's superior road holding and outstanding performance

which he experienced as a SAAB owner.

General Description

The car features a nearly pure aerodynamic body shell

of reinforced fiberglass weighing less than 100 lbs., yet

it is stronger than a comparable steel shell.  The light-

weight tubular steel frame gives the car a low curb weight

without detracting from the torsional rigidity that is

required in a sports racing machine.

Standard SAAB 96 suspension components are used along

with the SAAB engine and a four-speed gear box as standard

equipment.

Specifications

Engine - 3 cylinder, 2-stroke cycle, 841 cc, devel-

oping 42 bhp at 5,000 rpm with a maximum of 59 ft/lbs.

of torque at 3,000 rpm.

Bore - 2.760 inches

Stroke - 2.870 inches

Compression ratio - 7.3/1

Suspension and brakes

Four-wheel independent suspension with self sta-

bilizing rear axle assembly.  Damping is accomplished

with four hydraulic telescopic shock absorbers.  Total

AN358

brake lining area - 105 sq. in.

General

Light-weight reinforced fiberglass body shell.  Tu-

bular steel chassis with integrated sheet metal panels.

Front-wheel drive, counterclockwise engine rotation.

Price and Delivery

Tooling for the Quantum will allow production to

commence in the late fall of 1963.  The car will be mark-

eted through authorized dealers  and will carry the same

basic broad Warranty that the Standard SAAB car enjoys;

i.e., 24 months or 24,000 miles on power train, 6 months

or 6,000 miles on the remainder of the car.  Retail de-

livery price F.O.B. New Haven - $2,995*

*-Estimated Price - state, local tax, and trans-

portation extra.

THE QUANTUM SAAB

A prototype of a 1200 pound sports car has been

designed and built around the SAAB-96 engine by a group

comprising the Quantum Corporation.

The car features superior maneuverability, high per-

formance, reliability, and economy and smooth riding with

a clean aerodynamic body.

This is what gives the Quantum SAAB its superb char-

acteristics:  Front wheel drive, steel space frame, fiber-

glass body, proper weight distribution and low center of

gravity, neutral steering, excellent cornering and braking.

Specifications

Two cycle engine 42 HP SAAB-96...Rack and pinion

steering - SAAB...

Full instrument panel - SAAB 96...Independent

suspension - SAAB...

Heater and defroster...Three speed gear box - SAAB...

Pull-up side screens...

Wheelbase: 84 inches

AN358

Track: 48 inches

Road clearance: 6 inches

Weight (dry): 1200 lbs.

Mileage: 35 m.p.g. plus

Acceleration: (42 HP) 0-60 m.p.h./approximately 10

seconds

Engine: 3 cyl. - 2 cycle - 850cc - full roller bearing  		Ignition, brakes and accessories are standard SAAB

parts.

Seat belt and roll bar mountings included.

Windscreen and bumpers quickly removable for racing.

Competition

The design has been proven by two years of SCCA sports

racing and "Commuter Competition".  The car has turned Lime

Rock in 1:13, Marlboro in 1:50 and Thompson in 1:56 with GT

engine and tuning kit, Cerametallic brakes, four-speed gear

box, competition steering wheel, tachometer and racing

mirrors.

Manufacture

The steel space frame is fabricated by Eugene Engi-

neering, Inc. (Hyde Park, Mass.), one of the largest alum-

inum and steel fabricators in New England for the aircraft

and missile industry.

The fiberglass body is laminated by the Reinforced

Plastics Division of Atkins & Merrill, Inc. (Marlboro,

Mass.) the largest custom fiberglass molder in New England,

with years of experience in fiberglass for the transpor-

tation industry.

Personnel

Members of the group who have pooled their scientific,

engineering, and racing know-how to produce this machine:

Walter P. Kern: (MIT - BS, Temple U. - MS)--Manager of

Design, G.A. Philbrook Researches, Inc. (Boston, Mass.

and formerly Chief Mechanical Engineer, Nuclear Divi-

sion, Baird Atomic Instrument (Cambridge, Mass.)

Alfred C. Conrod:  (Tufts U. - BA in Physics)--Senior

Engineer, Instrument Technology Laboratories Division

of Itek (Lexington, Mass.) and formerly of Instrumen-

tation Laboratory, MIT.

John Suomola: (U. of St. Louis - BS, Aero Engineering) V.P.

for Engineering, Gabriel Electronics (Needham, Mass.),

and former staff member, MIT Instrumentation Labora-

tory.

Duncan Hay: (Drexel Institute of Technology, Philadelphia,

AN358

Penna, - BA in M.E.)--Mechanical Engineer at Magnion,

Inc. (Cambridge, Mass.).

Nathaniel C. Wiley, Jr.: V.P. Atkins & Merrill, Inc. (Sud-

bury, Mass.), Body design.

Quantums I thru V

The Quantum sports cars at JB Imports both carry a badge on the nose identifying them as "Quantum III."  The hub caps also sport a Q-III motif.  A similar badge on the nose of the Quantum Formula S open-wheeled race cars designates the model as a Quantum IV.  What were the Quantum I and II, you may ask?

The original steel chassis built by Walter Kern, Al Conrod and John Suomala was the Quantum I.  When that chassis was fitted with aluminum bodywork for racing, it was christened the Quantum II.  Kern says it was one of the ugliest cars on the track.

The sports car shown at the New York Auto Show in 1962 became the Quantum III, as were the two bright red pre-production cars which are now owned by SAAB Club members Bud Clarke and Jay Arruda of J & B Imports in Orange, California.

While awaiting word on the fate of the sports car, the Quantum company produced a race-car-in-a-kit to accommodate a SAAB drive-train (rear mounted and driving the rear wheels) and sold exclusively through SAAB dealers.  It was meant to produce a class similar to Formula Vee which used Volkswagen's 1200cc engine, four-speed transmission and stock suspension.  Fifty of the "Quantum Formula S" kits were produced.  SAAB Club member Tom Cox has tracked down about a dozen still in existence.

Another SAAB Club member, Jerry Jodice of Manchester, Massachusetts, has a sports car registered as a 1965 Quantum V.  It is actually a Ginetta, a British-built car that used BMC components.  Walter Kern added an Austin Mimi front end and the drive train from a '66 SAAB with the triple carbs.  He also installed a "Quantum V" badge on the nose.  Jodice worked with Kern in the late 1960s and the car was purchased from Kern.

The Ginetta is right-hand drive, has Recaro seats and the wheels are by Race-lite.  The chassis is made of chrome-moly tubing and it has a fiberglass body.  Total weight of the Ginetta/SAAB is only 600 lbs.  Today the "Quantum V" has 6000 miles on it, and could use some restoration work.