AN359

BETTER BRAKE BLEEDER

After reading Part 3 of the article by Dan Salvo on Brake Rebuilding/Bleeding for 95/96/97's in the April NINES, I thought I would propose an easier way to fabricate a "pressure bleeder" as follows:

Start with his "Obtain extra master cylinder caps (should only need on for the Sonett master cylinder reservoir & it will also fit the clutch Reservoir) for the system you intend to bleed and clean them scrupulously. Then go to your nearest cheapie car parts place or tire service center and get yourself a complete valve stem for a tubeless tire (including cap for that professional look). Make sure you have a drill bit that is the same size or only slightly smaller/larger than that stem's diameter where it will go through the cap. Measure for clearance and drill the cap, reclean it and install the valve stem (a metal stem will probably be easier to install than an all rubber stem).

Now we return to Dan's instructions at "Fill the master cylinder with brake fluid". Screw your just fabricated "pressure bleed system", nee master cylinder cap/tire valve, onto the master cylinder reservoir in place of the regular cap. Pump up the tank with a bicycle pump or your air compressor, you don't need a lot of pressure. Bleed away according to your manual, just remember to keep the reservoir full as possible with brake fluid. If you run it dry you will pump air into the brake system and get to do the bleeding all over again.

I know the DOT 5/DOT less than 5, hygroscopic brake fluid argument is still raging, but I change both of my road cars '74 Sonett (clutch system also) and my '73 Volvo 1800ES to DOT 5 fluid in '77 and haven't had any problems to date. The ES old brake fluid had in fact "hygroscoped" and rusted a rear cylinder which I had to rebuild (of course I did both).

I replaced the low number DOT stuff with DOT 5, "cause it strikes me that there is no need to remove water and other crap and corruption from a semi-enclosed system if there is nothing to suck the stuff into the system in the first place. Silicone is as inert as you can get, plus I don't sit in deep puddles and play with my brakes, so seepage due to cycling is of small concern to me.

Another trick for those of us who are still using their Sonett on the street, one you can do with mirror to a day/night unit out of a junk yard 96 years ago. All you gotta do is remove the screw from the back of the mirror head/roof mount and carefully, after spraying it with silicone or WD-40, pry the entire mirror head away from the mounting arm at the swivel. You will end up with the mirror/swivel (semi-shiny steel colored) and the flat black painted roof mount. If the swivel is rusty, you might want to remove the

AN359

entire assembly and do this at your work bench to be certain you don't scar any soft metal, as only two screws hold it to the roof.

[Just a reminder, SAAB says to use only DOT 4 brake fluid, not DOT3, which is sold at most parts stores, nor DOT 5, which is recommended for motorcycle use. The most common DOT 4 brake fluid is Castrol LMA. it may cost a bit more than DOT 3, but are you willing to risk your brakes, your SAAB, and or your life, to save a couple dollars.