AN371

UPLIFTING YOUR SONETT'S SNOOT

If your Sonett droops in the front, or if you want some extra clearance over fat 60 or 70 section tires, you can put in longer front springs from a 96 sedan.

Spring Wire

Year		Model	Diameter			Free Length

to-67	96		.46" (11.7mm)		15.4"

'67		Sonett	.46" (11.7mm)		13.3"

'68-'71	96		.48" (12.0mm)		15.9"

'69-'74	Sonett	.48" (12.0mm)		13.4"

'72-on	96		.49"	(12.2mm)		15.9"

Obviously SAAB used 96 springs and cut coils to fit Sonetts. I have used 96 coils many times in Sonetts to get a particular effect.

If you want to improve HANDLING, for autocross racing or similar use, use the late springs and cut to the ride height you prefer.

If you wish to improve RIDE, go for the earlier springs and use a stiffer shock absorber setting (a method used very successfully by Lotus for years).

In either case, I recommend using the sedan anti-roll bar. You will find part of the hardware for mounting the bar already on the lower A-frame of your Sonett. I also recommend that you install the bar when the engine is OUT of the car -- it's a BEAR otherwise. I also strongly recommend you use the factory tool for changing the coil springs, for your own safety.

Jack Ashcraft

NINES

Jan. 1990