AN372

HOT RUNNING 1500CC

The 1970, 1500cc, V-4 wagon that I drive runs hotter than before I had a total engine rebuild 30,000 miles ago, On a hot summer day and/or heavy load on the engine, the temperature gauge reads in the upper three-quarters of the dial, and I have had to stop to avert a boil over.

I have put in a new water pump and backing plate and had the radiator rodded out. When the fan bearing wore out, I put in a thermostatically controlled electric fan. None of these changes has had an effect. The coolant is clean and a 50/50 mixture. What else can I check.

ANSWER

Past experience would lead me to the radiator as the culprit. Although it has been cleaned, heat transfer from the tubes to the fins may not be as efficient as it once was. Before replacing the core with a new one, check the operating temperature with an accurate thermometer. Meat or candy kitchen ones work just fine!

Rob Perry

NINES

Feb. 1990