AN375

AIR FILTER FOR WEBER ICH

The old Solex or Ford carbs used on the V-4 are now very old and replacement parts is expensive. An excellent alternative is the Weber ICH at around $200.00. It bolts on directly without any manifold changes. Some linkage adjustments is necessary, and in cars with power brake booster it is necessary to add a couple of plumbing elbows to allow the PVC hose to clear the linkage.

The most recent problem I have had is getting a well fitting air filter that does not require a lot of modifications. (The stock filter will fit but the tabs that attach to the valve covers have to be modified or bent.) The large stock air filter also blocks easy access to the distributor and all else that it covers.

I have found an air filter assembly that works perfectly. It's a K&N #RA045V, and the box describes it as a "custom air filter W/vent, 2-1/16" ID FLG offset, 6" OD, 2"High, for Solex VW". I paid about $18.00.

A straight plastic vent tube, found in most discount auto stores, will be required. The existing vent hose cut slightly can be used. Most parts houses do not show an air filter for the ICH, but do show one for the ICT, which is what the K&N filter is for. The ICT, appears to be the same with the exception that the fuel line inlet faces away from the radiator.

David Kronen

NINES

Feb. 1990