AN376

AIR FILTER FOR WEBER 2-BBL

I have a '68 Sonett V-4, and put on a two-barrel Weber carb and manifold which made it run considerably better. Of course the air filter is a problem-no clearance.

I bought some fine wire mesh stainless doorscreen, fairly stiff, then cut that into an approximate shape of the bonnet "bubble", but sitting on top of the carb. Then close the bonnet, compressing the wire on any high spots. Make it as large as possible to increase airflow ability. Make sure the shape and size is correct, then cut a 3-inch aluminum tube (an old large Bosch fuel filter, cut up is great). Then fiberglass around the whole mesh, one layer on top, another on the bottom, making sure to glass in the 3-inch tube as well. Add more layers for strength.

Take a 3-inch dryer hose, attach it to the 3-inch aluminum tube, and route it back beside the heater box in the engine compartment. Attach the hose to any suitable air filter. I mounted a K&N unit right beside the heater box. With a bit of fancy sheet metal and ducting, a cold-or-warm air supply is possible.

This set up works great; there is no noticeable performance change with or without the air box. The cost is very little and doesn't take too long. I certainly think it's worth it to have filtered air, backfire protection and a lower noise along with the performance gain of the two-barrel carb.

Mark Hollingsworth

NINES

Feb. 1990