AN380

RX FOR A HOT V-4

I agree with DocNio about the possibility of a bad radiator core on Rob Perry's 1970 Saab 1500 V4 (NINES, Feb, '90) but there are more things to check:

First check the engine thermostat.  It should be no "hotter" then 180 degrees F (87 degrees C).  Next check the distributor for wear (shaft run-out), and that both the vacuum and centrifugal advance mechanisms work properly.  Dwell should be set to 50 degrees.  Make sure the engine timing is set correctly at 6 BTDC at cranking speed (not idle) with the vacuum advance hose disconnected.

I assume that Rob also checked the radiator cap to see that it holds the 4-6 psi it is designed to hold and that the plastic overflow tank has no leaks.

Finally, the driver must take care to keep the revs up when pulling long grades in summer heat.  Even an engine in perfect condition will tend to overheat if you lug it for a long distance on a hot day.

The last thing I would ask Rob Perry is about the type of gasoline he is using.  If he isn't using premium fuel, then the lower octane fuel in the tank also contributes to the overheat problem on a hard pull on a hot day.