AN382

TWO-STROKE TIPS

A lack of articles this month prompted a look in the old newsletters again, this time for help on 2-stroke SAABS.  Please note the information is 15 years old; some products mentioned may not be available.  TW

Replacement pressure plate

The clutch pressure plate can be replaced with a pressure plate from a 356 or 1600 series Porsche for super long life.  I have been using one for about 50,000 miles without one hint of trouble.

Build your own muffler

For better exhaust system performance, take off old connector pipe and rear muffler.  (Leave front one alone.)  Replace it with one you can build, or have built at low cost.  Cut old connector pipe and add a small glasspack muffler to it, bend it so it exits under the right door.  Doesn't produce anymore noise than stock system but it does help gas mileage and will last a heck of a lot longer than the stock system.

Ignition system

For the best bet, use NGK A-7 plugs for all normal driving.  THey seem to prevent loading up and fouling to a high degree.  Never use a hot plug and drive hard; this is one good way of burning up the engine.  Gap plugs .028 to .032, check and clean every 1000 if you can stand it.  Points and timing should be adjusted to Saabs own settings.  Plugs will last about 5,000 to 6,000 miles, with points lasting about 8,000.

To help prevent fouling, replace stock Bosch coil with Bosch Super Blue coil.  Probably need to add series resistor in the hot line to the coil, but this is an addition well worth it.

John Baird

Naches, WA

June '75

More ignition tips

The sparkplugs take a beating - best ones are ones made for city driving:

NGK have been used here for 4 years with a Mark 10 capacitive ignition system.  I set the plug gap to .040", not what the book says.  The Mark 10 puts out 40,000 bolts, but if the ignition wires arc, go back to .035".  This system lasted over 150,000 miles; distributor points were replaced after 68,000 miles.

The 96 has a pre-heater which snaps on and off the air cleaner.  You should always carry this in your car.  When the temp gets a little cool and it starts raining, the pre-heater should be on the air cleaner.

The car's thermostat should be replaced within a new one every other winter if it allows overheating.

The distributor is way out front and low, and tends to get we in rainy weather.  You can get a 1965 distributor with the hole in it and place a short hose on it.  If it stalls on the road in wet weather, remove the top of the distributor and dry it with a cloth.

Get rid of those carbon core spark plug wires and replace them with real wire-stainless steel wire, which has only 1/10 as much resistance as the carbon-core cable.  This is very important when you have a Mark 10 on your car.

Don Duda

Milwaukee, WI

Feb. '75

Distributor moisture

A simple solution for misfiring damp distributors that plague some Saabs from 1964 on down.  These symptoms appear due to the combination of the Distributor's extreme forward position near the grill and inclement weather.

To remedy this, cut a 12 inch piece of old tire inner tube intact, unclip the distributor cap off, insert the cap with its wires in the inner tube piece, snap the cap back on the distributor body and slide the piece of inner tube snugly over the cap and the distributor body's top, close the top by tying twine.  It is an effective and inexpensive shield against dampness.

Erice Severin

Akron, Ohio

Feb. '75