AN390

ADAPTING A TWO-STROKE WATER PUMP

Due to zero spare fan-shaft engine water pumps, I have been seeking an alternate.  (Ed. Note: The water pump on the earlier "fan-shaft" three-cylinder engines, 1956-64, is part of the generator.)

I pulled the pump out of a 1965 engine and found that placing it against the wider '65 generator bracket there was room for two mounting bolts and the pulleys lined up.  I drilled out the two 1/4" tapped holes in the housing to 5/16".  Then I ground about one-third off the heads of two 5/16" cap screws until they form-fit the housing and passed through the housing, backing plate and generator bracket.  The housing was rotated to point the inlet/outlet pipes at the right fender.  Eyeballing the generator bracket for best position, I marked the bracket for the 5/16" holes.  Grinding about 1/8" off the radius of the aluminum generator mount helped.

I used a triangle shaped plate to cover the half moon opening and drilled it to match the three holes in the housing that originally held sit to the head.  The design of the plate was to get as much coverage of the opening as possible; kinda cut to fit and grind to match.  Some 1/32" gasket material was utilized along with some "blue snot" for sealer, three more 5/16" bolts and everything was tightened nice and even.

The next problem was getting hoses to fit.  I used a 1" to 1/2" reducer of copper water pipe (the O.D. size is about 1-1/8" by 5/8" and will mate the '65 radiator hose with the 3/4" radiator hose used on pre-'65 engines.  I used the '65 hose and part of the outlet pipe to hook up to the hose going under the engine.

The temp gauge sez I'm on the right track.  I've got a few hundred miles on it now and will drive to to Milwaukee for their Show-and-Tell meeting end of June.  If it hands together, you'll see me and Sadie in Massachusetts in August.