AN395

V-4 BRAKE MC ALTERNATIVES

Several months ago the brake master cylinder in my '68 96-V4 failed--fortunately the car was moving very slowly at the time!  I looked into getting a replacement master cylinder and found that it would be fairly expensive, and the replacement cylinder would be among the last of the Mohicans.  This left me wondering about the long-term outlook for availability of the cylinders.

Glen Edinger of Redmond, Washington, who's been servicing my 96 for the last few years, said he's successfully installed the post-'68 master cylinder in the earlier 96's.  This master cylinder is shared with early 99's and should be available for a long time.  The conversion also gives you power brakes.  However, it entails cutting out the part of the firewall that carries the master cylinder and welding in the corresponding part of the firewall from a later car.  It's best done when the engine has to be removed for some other reason anyway, which wasn't my situation.

I wound up having my master cylinder bored out and then sleeved back down to stock bore with brass.  The work was done for roughly $50 by White Post Restorations (White Post, VA  22663, phone 703-837-1140).  Since White Post's mainline business is restoration of classic cars such as Rolls-Royces, Pierce-Arrows and Duesenbergs, I felt they were certainly good enough to work on a SAAB master cylinder!

Cylinders to be sent to White Post should be completely disassembled.  You'll receive special fast service at no additional charge if you enclose a note stating that the car is your daily transportation.  My master cylinder arrived back in Seattle six day after if left, traveling by UPS Second Day Air both ways.  With regular changes of brake fluid it should theoretically last indefinitely.