AN4

TWO-STROKE TIPS

My '63 was making a kuklunka-kuknocka sometimes during acceleration and when hitting bumps and potholes, and I suspected that the front U-Joints (technically they are constant velocity joints) were getting worn. On the older 3 cyl's there's 2 steel clamshell encasing 2 rubber donuts, and the donuts transmit the energy smoothly from the gearbox to the driveshaft and absorb the slight change in speed that a universal joint undergoes as it flexes and changes the drive angle. The ability to absorb this change in speed is what makes it a constant velocity joint. Anyway, I had let 'em go for a long time because it looked like changing 'em was a very hairy job, but it's really quite simple: first, remove the hood. On an old 3 cyl. this is a matter of unhooking the headlights, horn and windowshade and releasing the hold down strap. Be careful with the strap or the whole darn thing will flop off the car, onto the driveway and maybe bust a headlight. On the new 3 cylinders, forget it. They don't have these kind of U-Joints anyway.

Once you learn this trick, doing almost anything under the hood of a 3 cylinder becomes much easier. OK, then slit the clamshells (4 bolts and a barlow knife) and slide the axle as it will go. Then loosen the bolt in the middle of the gearbox end of the joint and slide it out of the gearbox, just pull the whole thing out. Now this makes it sound easier that it is, but it can be done, without so much as jacking the car up. It can be done with all 4 on the ground. It is just real crowded in there and it takes a lot of fiddling around, but it can be done, in about an hour each side. At this point, just change the rubber pieces and reassemble. Don't try to use old ones, go ahead and get new ones- it makes an enormous difference in the feel of the car. If you let 'em go too long, the inner part of the joint will tear up the clamshell and cost you somebucks. The P/N for the donuts is 7011844 they cost about $4.00 each and you'll need 4 of them to do your 96.

The U-Joints hadn't been fixed a week when, emboldened by this success, I decided to tackle my chronic overheating problem. To make a long story short, it turned out to be that the head gasket was very slightly blown (I know this sounds like being very slightly pregnant, but I swear it was just barely leaking, it wouldn't even show up on the compression test). But I replaced it with a good new original SAAB gasket (the funky one was from JC Whitney) and torqued it in accordance with the timetable on the package and it runs strong, cool and quite.

As for the question of oil, there are, generally, 2 major types of two-stroke oil, as you'll find them on the shelf at you friendly local parts store, motorcycle oil and outboard oil. They almost always have different part numbers, and there's more to it than just packaging: M/C oil is for running in motorcycles and the head temp on motorcycles is very high, especially compared to the efficient, cool-running SAAB 3 banger. Outboard oil is for cooler-running (watercooled) outboards, and load conditions that more nearly approximate that of the car. I strongly suspect that M/C oil would not burn as completely at the lower temperature and produce a tendency to foul plugs. I know this to be true of outboards using M/C oil, but have not actually done it with my 96 yet.

The Boating Industry Association has very high standards for two-cycle oil, and those wishing to safeguard their engines from cheapie oil would do well to use only BIA approved oil. Also, in a two-stroke engine, detonation is a very destructive force, as any 3 cylinder owner who has ever gotten his gem out of timing will at test. The obvious answer to keeping the big "D" from wiping out your two-stroke is to keep it timed and tuned right, of course, but a little extra road insurance can be purchased in a form of premium gas.

Premium gasoline has a higher octane rating than regular and all that means is that it has a reduced tendency to detonate, or knock or ping as it is sometimes called. It is not more explosive and more volatile than regular, it does not run hotter (it runs cooler in fact because it burns more efficiently) and it will not "burn up your engine "as some ill-informed folks will tell you. On the other hand, the 3 cylinder doesn't really need it, it won't do anything for your performance, only difference you'll notice is that you car will run a little cooler than usual and perhaps get microscopically better gas milage.

Also if your water pump develops a leak at the seal, fix it at once, because the water will eventually unlubricate the back bearing in the generator and the bearing will grind itself up and maybe the expensive-and-ever-so-hard-to-find armature with it. Mine sprung a leak last year and the bearing just went out last month. the bearings in the generator, front and rear, are fairly common in the USA, it's Delco # (NDH Bearing) is 77502 and under that was the legend Ball Bearing 954293. Don't try to hammer the aft bearing off, take it someone with a hydraulic press and lots of experience pressing stuff on and off. If you hit that dainty little shaft with anything harder than an intense stare, you'll regret it, I promise you.