AN418

TRANSMISSION LUBRICATION

Please present this question to the SAAB wizards and gurus of our membership:  What lubricant should we use in the transmission?

Ted Tucker's lecture, as it appeared in the Newsletter specified Texaco multi-gear lubricant EP80 GL4/GL5.

Robert Wehman (of Intercontinental Lubricants) states that SAE 75W-90 API GL5 is adequate for the Sonett transmission.

Local wizards suggest Valvoline SAE 80W-90 EP with enough Marvel Mystery oil to make it "smell right."  One 2-stroke enthusiast defined the correct mixture of the above as "using the gearbox dipstick (a SAAB transmission tool which is now apparently unobtainable) fill to the low level mark with gearlube, fill to the full mark with Marvel Mystery oil.  The Marvel Mystery oil label instructs one to mix in at 10% to 20% ratio to "winterize" crankcases and gearboxes.

Listen guys, I live in a farm community not far from the state capital (tractor suppliers and hi-tech lubricant wholesalers) and EP80 is a special order, 55 gallon drum minimum, commodity.  That's if one can find a supplier.  I've got relatively low mileage transmissions (one with 34,000 miles, one with 8,800 miles) and I don't want to experiment with lubricants and chance damaging my machinery.  55 gallons is 110 oil changes.  Anybody want to Share?

(One point of Ted Tucker's lecture on the V4 transmission was to day don't mess around when you change your transmission lube--use what SAAB said to use.  I just rechecked the Owner's Manuals from 2967-1974.  They start with EP SAE 80 and end with EP SAE 80 (API GL5), which is to say they start and end the same way.  In 1967, I don't believe the API (American Petroleum Institute) had any gear lube ratings.  By 1974, they did.  Ted found one source, Texaco.  It is surely not the only one.  Multi-viscosity gear lubes also are relatively new.  For example, the Intercontinental 75W-90 should be adequate.  I'm especially sure of that since Bob Wehman said so (BWSS, that' rule number two.)  I'm less sure that the 80W-90 Valvoline is OK, but it probably is.  I have no confidence in mixing in some unknown amount of that famous elixir Marvel Mystery oil "until it seems right."

What you need: the gear lube you use has to meet all of the following, SAE 80 viscosity number.  A multi-viscosity version should be alright so long as it spans 80.  "EP" stands for "extreme pressure."  Bob Wehman has told us that API GL5 includes the equivalent of EP.  So, if you don't want to order a 55-gallon drum or can't find a few fellow SAABers to go in with you, I suggest you try the nearest Intercontinental Distributor.  Unfortunately, they

AN418

aren't very near:

Spectro Oils of Ohio

41970 Oberlin Road Route 20

Elyria, OH  44035

(216) 323-3051

Failing that, contact Walter Kern with your needs.