AN419

IT BEGAN WITH SO NEAT WITH SONETT - PART III

by

Carl-Ake Blomstrand

Translation from Club Sonett Sweden Newsletter

No. 2, 1988

by

Bjorn Collin

The problems (of car manufacturing) were not acknowledged in the early days.  The "scheduled production" got off to quite a slow start.  No production quota bonuses were established for obvious reasons.  The different assembly stations had to be properly tuned and timed to start with.  There was no real pressure for time during the early period, so we did not reflect too much over the problems that surfaced, and there was a fair amount of time available to overcome the difficulties.  It became a different story when the efficiency experts came into the picture.

To start with, it was discovered that some of the protruding parts on the engine did not clear the chassis.  That was easily fixed by making a couple of small holes for clearance.  The problems with lack of precision for the sheetmetal parts, that I mentioned earlier, were also present, but these were also corrected after a while.  Unfortunately, these problems made me somewhat unpopular in some circles, however my opinion was that I was not there to win a popularity contest, but to help build a good car.

I reacted at an early stage to the fact that the wiring harnesses were attached with a type of clamp identical to the ones used in home construction.  (These were made of white plastic and quite large.)  I did not think these belonged in a car, and they were also too time-consuming to install.  When the design office wondered how else to attach the harnesses, I had to explain that the automobile industry was spot welding metal strips to the chassis at suitable placed, and these were simply bent around the harness.  This practice had been common for the last 5 decades and the installation went much faster.  This was then immediately accepted and the first chassis with this modification arrived from the metal shop.  However, something had gone wrong.  The metal strips were not necessarily where the wiring was supposed to be routed.  The shop probably had not received any drawings, or they thought it did not matter that much.  Well, even this was corrected after a while.

The trunk lid; dear me.  A small, neglected little detail was hardly more then a mailbox lid.  The designers should not take the blame for this, however.  It really was an emergency solution because they did not have time enough to design an opening rear hatch.  That did not come until much later.  The problems with the

AN419

trunk lid was that it was quite weak and closed with a simple turning handle.  It took a long time before we found a sealing gasket that was thick enough and soft enough so that it did not excessively.  The lid bent visibly when it was closed and I don't think that it was ever leak free, but it was really bad in the beginning.

The engines were very well protected when they arrived and also contained quite an amount of oil.  This oil had to go somewhere and it was sucked straight into the car through the trunk lid if one drove the car before the oil was consumed.  It almost became like a gas chamber and one could hardly see the instruments in the dashboard.  This problem was partially solved with the help of SAAB, and I will come back to this later.

Another detail which did not cause any real problems, but was responsible for quite a lot of play, was the small ball joint between the gear selector shaft in the gearbox and the shaft from the gear shift on the steering column.  Both ends of this ball joint are fixed in position with conical pins, to the holes had to be at a certain angle to each other for the gearshift to be in the correct position.  I lost count on how many ball joints with different positions of holes we received from the mechanical shop before they finally got it right, and I don't think there was ever an attempt to measure the correct angle between the holes.  Somehow we were left with the impression that it was strictly a trial and error procedure.  The ball joints were not very expensive.  In all honesty, it must be said, that the relatively large movement of the gearshift resulted in a very small movement of the gear shaft in the gearbox, and therefore the location of the holes needed to be precise.

I have one more example of a small detail that clearly shows the lack of understanding of quality that some people at ASJ had.  The trunk lid was closed with a simple turning handle.  The handle and lock were purchased as an assembly.  For some reason this did not include the little bracket that actually held the lid in place when it was closed.  This bracket was manufactured by our own mechanical shop using a flat piece of iron about 3 X 15 mm and 45 mm long.  In one end a square hole was punched to fit the turning tap on the handle, and the other end was rounded and phased.  The material for this must have been stored outside for about 10 years judging by the severe rusting that had taken place.  Even the zinc plating could not hide the severity of the rust.

The rounding and phasing was done by hand using a coarse grinder.  The rounding was not one radius but more like four different radii.  I showed Bjorn some examples of this and asked if we should install them.  He did not think so, and all of these pieces were scrapped with the exception of the one which I kept as a souvenir in case

AN419

someone didn't believe me.

The front and rear windows were big problems.  It was very difficult to get these in time.  If I recall right, the first windows were manufactured in Belgium.  The first cars had to be fitted with rear windows made of acrylic plastic, and for some reason these windows did not fit very well. In fact, the bodies were not quite straight if one compared them with the windows.  In order to fit the windows, we sometimes had to use a hydraulic jack to "straighten" the body, and I was surprised that the windows did not pop out when the jack was removed.  The tension must have been great.  The reason for the "crooked" bodies was often discussed.  There could be two reasons: either the mold for the body was not straight   to start with, or the body had changed shape under its own weight during the hardening process.  It takes quite a while before the plastic becomes fully cured, and I bet on the latter explanation.  The molds for the windows were made after the original body mold and consequently they did not fit the cured body.  It remained a mystery, however, why all bodies were bent in the same direction.  Was it possible the mold was the culprit?  I suggested time after time that a mold be made from a body that was fully cured after the oven bake following painting, and I was finally proven right.  We did not have any more problems with the window installation after that.

The plastic also caused us another problem in the beginning.  The techniques used when working with glass fiber reinforced plastic were nothing new, but could cause problems with a lack of experience.  For those who do not know about the art of molding fiberglass, it may be appropriate to provide a simple explanation.  First, a model of wood or other suitable material is made for the mold.  The mold is then produced in glass fiber reinforced polyester hartz material.  Sometimes reinforced of wood or aluminum are incorporated to prevent weakness or dimensional changes.  After adjustments, grinding and polishing, the mold is ready for casting the appropriate piece.  To prevent the cast from permanently attaching to the mold, the mold is coated with a material which usually is a water soluble polyvinyl alcohol.  The piece to be cast, in this case the body, is then built up using several layers of glass fiber mat which are bonded together with polyester resin.  The resin is relatively easy flowing and fills in the crevices quite well.  A special tool is used to eliminate air bubbles during this process.

One thing that was missed in the beginning was to start the building by using gelcoat as the first layer.  This is a thicker polyester resin which can be applied a couple of millimeters thick and not run.  The gelcoat layer provides an outer layer free of glass fiber more easily adjusted by grinding and polishing.  The lack of gelcoat was probably the reason for difficulties painting

AN419

the bodies.  We discovered a lot of small, crater-like pores in the paint.  We were never sure of the reason for this, but my theory was that the bodies were not fully cured when they were painted, and the painted bodies were dried in an oven.  The higher temperature probably caused an accelerated curing that produced a gas that found its way out between the glass fiver mat and the still soft paint layer.  The result was the pin head sized craters.  The heat in the oven could also have caused the bodies to soften so that they changed their form.  The gelcoat probably prevented further migration of the gas, and after the bodies had been stored for curing prior to painting, these problems disappeared.

This went off the track a little bit, but it may be an explanation for those Sonett owners who need to make repairs to the body.  Some of the details, like the rear lid and covers for the air outlets on the side were press molded using a glass fiber/resin mixture.

to be continued...