AN420

WALTER'S WORKSHOP

Chassis Flex and Doors the Questions

Walter, I recently read an article in Volume IX Number 2 about the replacement of rocker panels under the heading "Our British Connection Checks In."  Currently, I plan to replace both of my rocker panels on my Sonett III in the next month or so.  I really didn't know about the chassis flex problem involved here.  After reading the article I'm still left in the dark as to how to support the chassis in the right places before the removal and then the installation of the rocker panel.  I was wondering if someone within the Club could provide some detailed sketches on just exactly where one would support the chassis before and during the removal and installation of the rocker panels.  I would really appreciate some detailed sketches as well as any additional information on doing this job.

I am currently replacing a door skin on my Sonett III and I have noticed that the pop rivet holes in the used skin do not align with my steel door frame drilled holes.  Is there a means of alignment for the skin to the door?  Or is it a trial and error situation?

Chassis Flex, an Answer

I have had two passenger side rocker panels replaced by Dave Hosmer while I watched.  I called him this morning to check my memory of the procedure he used which was completely successful.

The strong recommendation is to replace only the outer rocker panel by cutting it just below the line of the door fiberglass.  If you then weld along this line with out without an offset, the joint does not show unless you look up at it.  This is then stronger than the original if you use a MIG welder and is very safe with regard to disturbing chassis alignment.  Use 16 ga. steel which is a heavier gauge than the original and use ZRC zinc primer as the undercoating.  You can then use a tar undercoat spray later.  Dave tells me that he has seen your car and this will work for you.  You will need a floor pan patch on the driver side, but that can be added along with the outer rocker panel.

As for the correct jacking procedure, if you do as outlined above, the risk of flexing is greatly reduced.  The places to do the lifting are shown below in a sketch.  If the lift you use is placed as shown, the frame will be supported at the four diagonals of the center section (close to the ends of the rocker panels.)  If the lift will not do this and leave working room along each side, use the lift to raise the car enough to place 55 gallon drums under the rear wheels, letting the car stand on it wheels normally.  Dave has done one each way for me with no noticeable difference in the

AN420

result.  End patches should be welded on the ends, since that is where a lot of the saltwater gets in.

The holes in the door skin will probably not line up, so the best thing to do is use the holes in the skin as guides for drilling new ones into the door frame.