AN423

WALTER'S WORKSHOP

I recently had the clutch on two Sonett III's stick in the engaged condition.  In order to release the stuck condition without separating the engine and transmission, the following is recommended by Bud Clark.  Since 1st and 2nd hears are on the secondary shaft in the transmission, which is weaker than the main shaft in terms of its torque rating, the procedure should be done in 3rd gear.

First, start the engine with the transmission in neutral.  When a the engine is warm, shut it off, then depress the clutch, shift to 3rd and restart the engine.  (With the engine warm this should be possible.)  The car will move and if you apply the brakes and accelerate moderately, the clutch should break free.  Of course, you should be sure to do this with enough space to move the car.

A similar procedure was recently reported in NINES but recommended 1st gear.  We think it is less likely to cause transmission damage if you use 3rd gear.  Should using 3rd gear fail, you can always try it with 1st or 2nd to get more torque, but remember that there is a greater risk of damage to the secondary shaft than to the primary.