AN426

V-4 SHIPPING CRATES

So you bought a V-4 engine and don't know how to get it shipped? Send the seller this article. He can  make up the simple crate shown out of 2X4's, 2X3's and some 3.5" nails, a pc of steel angle and 5 lug bolts. All the lumber up to the engine mounts is 2X4 stock. Note a short pc of scrap 3/4" plywood was used under the engine mounts to level the engine. The uprights are of 2X3 stock. The cross pcs at the top are 2x3 and these are lag screwed in place so they can be removed to make it easier to remove the engine upon arrival.

The lag screws thru the engine mounts and the angle at the rear (which is bolted to the flywheel with a metric bolt) just to keep the engine located in the crate during shipping.

Drain the oil before shipping. It's also a good idea to plug all the holes into the engine with plastic plugs to keep dust out during shipping. Finally, cover the whole mess with a heavy garbage bag or a garden plastic and staple it in place. I also put a tag on the engine inside the plastic telling the address of the sender and recipient just in case the one outside gets lost.

This is a good way to ship the 280 lb V-4 engine and the crate can be used any number of times unless the fright company destroys it during shipping.

AN426