AN429

LET'S NEUTER IT!

I had several calls lately about neutering the Saab 95/96/97 transaxle.  I've also seen some horrible, welded-up examples of how NOT to do it, so here is the way to do it right.

The transaxle must be out of the car, drained, and cleaned thoroughly.  Knock out the axle drivers (see Fig 1) and remove the bell housing bolts. Don't forget the single bolt on the top right that faces rearward.  Remove the release bearing.  Use two screwdrivers and gently separate the bell housing from the transaxle.  Be sure to collect the small needle bearing on the end of the clutch shaft that fits inside the freewheel hub of the transaxle mainshaft.  Once the bell housing is off you do not have to anything to the transaxle unless you need to do work on it due to noise, hard shifting, etc.

Remove the bolt on top of the bell housing that holds the freewheel control (see Fig 2).  Remove bolt, spring, washer and control.  The ball bearing may or may not come out of the bolt hole.  Don't worry about it either way.

Using a seal removal tool, remove the front seal from the clutch side of the bell housing (item 1, Fig 3).  Using a compressing snap ring pliers, remove the large snap ring behind the front seal (see Item 3 Fig 3).  Using an expanding snap ring pliers, remove the snap ring at the extreme aft end of the clutch shaft (see item 10, fig 3). Push the clutch shaft forward, out of the bell housing.  Collect the freewheel control fork (item 8) and the freewheel clutch gear (item 9) as the shaft is pushed out.

Now clean everything thoroughly.  The bell housing shaft, the gear.  Check the bearing--spin it--if it makes any noise, remove the front snap ring and replace the bearing with a new one.

Now is a good time to inspect the release bearing control arm for excess wear at the points shown by arrows.  If you find more than 1/16" of wear the release arm should be replaced (we do supply rebuilt arms--see our ad next page).  Also check the release bearing--spin it--for noise.  Replace it if it is noisy.  Now for reassembly.

The freewheel neutering device is a simple sleeve cut from 1" pipe with a pipe cutter, not a hack saw, that is nominally 27mm long.  Nominal is the correct term.  In some transaxles this is just the right length.  Others need a sleeve just a bit shorter due to differences in production tolerances in these transmissions.  More on this later.  Slip the neuter sleeve on the back end of the shaft, then the freewheel clutch gear. Check that there will be clearance for the aft snap ring to be installed (item 10, Fig 3).

AN429

If so, remove the gear and the sleeve from the shaft.  I assume you have the bearing you want in place on the shaft and that both bearing snap rings are in place.  Insert the shaft from the front of the bell housing.  Install the large front snap ring.  NOW install the neuter sleeve, the freewheel clutch gear and the aft snap ring onto the clutch shaft.  See Fig 5.

Replace the side seals on the bell housing.  Don't whine about how good they look.  Replace them.  Now thoroughly clean up the mating surface of the transaxle.  Lay a quarter inch diameter bead of hi temp silicone in the groove of the transaxle (See Fig 6).  Fill the depression in the inside of the side seals with white lithium grease (See Fig 7).  Reinstall the small needle bearing onto the end of the clutch shaft or into the freewheel hub so it does not get lost.

Fit the end of the clutch shaft into the freewheel hub of the transaxle and wiggle the bell housing and transaxle together.  Install the bolts and snug the bolts down.  Now take a look into the hole on top of the bell housing where the freewheel control used to be.  Use a screwdriver or similar tool and check that the gear has about 1mm of fore and aft free play.  If it does, torque the bolts (16 foot pounds).  If it does NOT, take it all apart and the file off the neuter sleeve an appropriate amount until, when you make this check, the IS 1mm of free play.  You MUST have this amount of free play to assure that the transaxle does not bind up when it gets hot and everything expands.  When you finally get it right, then torque the mounting bolts to 16 foot pound.  See Fig 8 for the view into the bell housing.

Now you can install the front clutch shaft seal, the release bearing, and the cap and gasket to cover the hole in the top of the bell housing (we provide a neuter KIT that contains all of the necessary parts--see our ad this page).

Now is a good time to check the condition of the rear transmission mount in the car and replace it if it is cracked , oil soaked or sagging badly.  Level the transaxle and add oil until it runs out the oil level plug on the side (about 4 pints of fluid).  I recommend AMSOIL 75/90 GL5 translube, as I have used it for years with not problems of any kind.  It also tends to make the gearbox shift easier and tends to quiet them down in time.