AN430

DEBUNKING LEGENDS ABOUT THE V-4 GEARBOX

The following is a transcript of a talk given by Ted Tucker at the 1985 SAAB convention held in Chambersburg, PA.

When Carolanne (Curtis) asked me to come up here, I thought we could put a gearbox in the Mule (our Chevy pickup), and the bench, jig, and various tools and show you how to rebuild one.  But, having you come to my shop and having me come to Chambersburg is a big difference, and I decided I wouldn't do that.  So, rather than tell you how to tear the gearbox apart and repair it, I thought possibly I could persuade you to treat the gearbox in such a way that you won't have to repair it.

(Audience member) "Too late now!!"

Well, now I'm going to primarily talk about the 96 family gearbox.  If you're a 900 person and you don't recognize the 96's as SAAB's, why, you can take off.  However, they do have some things in common, but they are distinct enough that it is foolish to lump all Saab gearboxes together, and you can get into all kinds of trouble if you don't recognize and respect those differences.

The 96 gearbox is an extremely efficient piece of machinery.  The reason is that the Saab people, when they began the project of designing a car, had never built one before, but they'd designed lots of airplanes.  And, of course, airplanes are extremely efficient machines, or the damn things wouldn't fly! So, the Saab people were concerned with efficiency, and the gearbox shows it.

Witness the fact that every bearing in the 96 gearbox is a ball bearing, except one.  Ball bearings are at least four times as efficient as roller bearings.  But, they require four times better care, or proper lubrication.  It takes a heck of a lot better lubricant to successfully oil a 96 type gearbox with ball bearings than a 99 type box that is primarily equipped with roller bearings.  Let's consider bearing failure and its most probable causes.  The calculated life expectancy of any bearing is based on the following four assumptions:

1.That good lubrication in sufficient quantity will always be available.

2.That bearings will be mounted without damage.

3.That all parts dimensions related to the bearing are correct.

4.That there are not defects inherent in the bearing.

Failure to meet conditions 1 thru 4, in whole or in part, can

AN430

result in:

A. Spalling, which is the crumbling of metal.  It is caused by incorrect load range, faulty fitting of a bearing, or inadequate lubrication, all of which, singly or in concert, can cause premature bearing failure.

B. Parasitic loads, caused by cocking, pinching, and other sloppy bearing mounting practices, or by too high or too low torque on securing nuts, especially where the bearing is not secured by s shaft shoulder.

C. Smearing is when the oil film between  moving surfaces is inadequate, allowing undue friction and high temperatures.  High enough temperatures can actually pull metal from one surface and weld it to the other.  Smearing leads to spalling, and spalling to failure.

D. Use only first quality bearings and parts to avoid conditions 3 and 4 above.

The bearing assortment of Saab 95, 6 or 7 gearbox consists of three ball bearings on the Primary shaft (input).  The Counter or "intermediate" (Saab name) shaft is mounted in two ball bearings.  The Pinion Shaft is mounted in a double-row ball bearing in the rear and one lonely roller bearing in the front supporting the pinion.  There are also ball bearings on either side of the differential, for a total of eight ball and one roller bearing.  Depending on the year of manufacture, there are either six or eight needle bearings in the transmission.  What is startling about this is that we could carry our examination on through the original engine and running gear and find no other roller or sleeve bearings.

That, my fellow Saab-snobs, is dedication to efficiency!  It also accounts for a 25HP FWD corn-popper clobbering the world's auto elite at their own game.

Let's talk about Elastohydrodynamitism.  Elastohydrodynamic film is the tern used to describe adequate lubrication.  Viscosity, always a much maligned word, is, according to Ingersoll Rands' Cameron Hydraulic Date, "that property which offers resistance to flow, due to the existence of internal friction within the fluid."  This resistance to flow, expressed as a coefficient of dynamic (or absolute) viscosity, is "the force required to move a unit area a unit distance."

The most widely used system of measuring viscosity is the Saybolt, which measures the time in seconds for a liquid to flow  from a filled container of specific dimensions through one or two orifices in the bottom of the container.  The resulting numbers are units

AN430

SSU (Seconds Saybolt Universal).  The efflux (a fancy word for exit or pour) time in seconds is converted empirically to kinematic viscosity in other units.

The foregoing paragraphs are not designed to confuse you.  Only to illustrate the fact that to lay people lubrication can be a very slippery subject.

Early on, Saab-snobbers need to appreciate,  or fear (and still do), a history of frequent failure of the 96 gearbox.  This, not withstanding Saab's worldwide reputation for both efficient and reliable design.  It was an enigma difficult to explain or avoid.

The gearbox was often referred to as a "weak link" in the car.  That is a bum rap.  It is not a weak link.  It is a very fine machine, but it requires better care because it is a better machine.

After rebuilding several hundred 96 transmissions, I caught on to the fact that "the weak link in an otherwise nice little car" was a cop-out for those who hadn't a clue; or a convenient excuse for those who should have known better and didn't.

The sulphurous smell of 90-140 gear lube caused me to sneak a sample through the Saybolt Viscometer at a local university engineering lab, and it confirmed my suspicion that the unfortunate little guys were literally being strangles to death by lubricants 20 to 100 times more viscous than the EP 80 for which they were designed.

I'm sorry to report that my investigation of the matter turned up several cases of old line, well-meaning, great reputation but sinning Saab dealerships.  One was a Saab/BMW dual dealer whose parts man parts man stocked only EP 80-90 in the belief that what was okay for the Bimmer was bound to be good for the Saab.  Yet he was putting gearlube into 96s that was 78 times too viscous for the 96 box! God only knows how many he killed.

Another case involved a gearbox I rebuilt for a gentleman in Maryland.  He picked it up, and with the gearbox I gave him my usual 2+ quarts of EP 80 in a jug.  He took the box back to an old line Saab dealer I'd known for more than twenty years, (for installation), and the service manager looked at the jug I'd provided and asked, "What's that crap?"  (It was written right on the side in grease pencil "EP 80".)

I don't put any of that in 96 gearboxes, I use 75 weight, that's what all Saab's use!"  The owner of the car was really upset about this, so he called me and asked me what he should do.  I had him drive to the nearest service station and have the 75 weight drained

AN430

and the box filled with the EP 80 I'd provided.  That's been about five or six years ago.  Last Christmas I got a card from him.  He thanked me for the gearbox, said it's been going great, and he wants another load of EP 80 so he can change it himself.  Now, if he had put 75 weight in there, he would have destroyed it.  EP 80 is twenty times more viscous than EP 75!!!

After finding that out, let's not fiddle around with EP 75 in the 96 gearbox.  Twenty times is just too much!  The relationship of viscosity from one gearlube to another is obviously not a linear progression.  You know, the difference between the number 75 and 80 doesn't seem that much.  But to find out how it's arrived at, you have to mix the damn stuff and then a Saybolt viscometer and see what you have.

As I say, if Saab made a bad transmission, if the 96 box is a weakness, I's admit it.  But it's not.  Airplane people are going to make very fine things.  You won't find a gearbox set up with the type of bearings you find in a 96 made by anybody today, including Mercedes or Rolls Royce.  It's just too good for those people.

The thing to remember from all this is to use EP 80 made by Texaco only.  When I first opened Loki Automotive I had a hell of a time finding it.  I finally found that Quaker State also refines EP 80.  I got about 20 gallons of it.  The first time I had to tear down one of those gearboxes, it had so much soot (ash) in it that I said I had to find a better oil.

Finally, I got a hold of a lubrication engineer from Texaco, and man, they've been making this stuff for years and it's great.  It's full name ins "Multi Gear Lubricant EP 80, for service GL4 and GL5."

(Editors note: Texaco no longer offers EP 80, only a multi-weight gear lube.  See separate article on currently available lubricants for 96 series gearboxes.)

Question:  "I've heard EP 75 was introduced to provide better lubrication at lower temperatures.  From what you're saying, is it too thin to properly lubricate a 96 (also 93, 5, and 7) at any temperature?

Any temperature.  People in extremely cold climates will say, "We put kerosene in to lighten it."  In extremely cold climates like the Arctic Testing Circle in Hudson Bay, it is so damn  cold that it will congeal the oil solid, I don't care what the rating of the lube is.  But if it's gonna congeal, make it EP 80, because when you get to an area where it will be warm, it won't be a dead gearbox.  If you put anything in there to dilute it, by the time

AN430

you drain it out, you probably have done some pretty severe damage.  Gearlube is inexpensive, transmissions are not.

The 96 family transmissions are all gone now.  There are no new ones available.  So we gotta take damn good care of the ones we have, because there aren't going to by anymore, at any price.  Even good used ones are getting a bit scarce.  I like Saab's.  I've been a Saab-snob since 1962, and I wouldn't have anything else.  And I'd like to help everybody.  But even if I've made you really ticked at me, I hope I've impressed you with the fact that gearlube is the most essential thing in that gearbox.  Change it every year if you want to.

Question: Is that important?

It's that important.  Change it every year.  I do. Considering where we stand today, do it every year and your gearbox will outlast your engine, I guarantee you.  And I don't care how hard you treat that gearbox.  You take good care of it and it will survive.  I rebuilt a gearbox for my son four years ago.  He's running a Sonett in F-Production.  He won the Southeast Championship in autocrossing three years in a row, plus he's been running hill climbs and other things.  He pulled the box this year, and I gave him another gearbox, and yet there is nothing wrong with that original gearbox.  It does not need overhauling.  It does not need any new bearings.  He's going to use it in his 96.

Question: Do you have any experience with synthetics?

I don't believe in them.  It doesn't say "EP 80," it's not gearlube as far as I'm concerned.

I don't want to start arguments with people.  It's

just that I've seen so many cases where it has done the job.

Question: How about using freewheel?

I love it.  But in 1969 Saab went from the 6-roller freewheel to a 10-roller hub to overcome objections from the public about the freewheel being too abrupt.  Instead of having six hefty rollers and six hefty springs, they put in ten tiny rollers and two springs per roller to equalize each other, and it became a very fragile thing.  What I do for people who like to use freewheel is get a 6-roller for them.  You can't buy a 6-roller unit (complete) new any more.  But the rollers, springs and sleeves are still available.  I buy a lot of junk transmissions just to get the 6-roller hubs out of them.  The free-wheel from a 93 will work beautifully in a '73 96 or a '74 Sonett.  They're so durable that you can generally just clean them off and put them in and they'll go.

AN430

Question: I've been told that not using my freewheel can lead to problems.  Since I'm not fond of using  it, am I asking for trouble?

Not if it's positively locked out, 100 percent.  You get into trouble when the late-style nylon lever atop the trans gets worn or loose, or the hole containing the  control rod coming up from inside the box gets elongated and sloppy.  It's this slight misengagement that can cause an in-and-out action, and mismeshing and wear to the teeth in the "clutch shaft gear," as I call it.  This is more of a problem on the 10-roller unit.  Just be sure the lever is in good shape and tight, and you have the control rod T-handle pulled all the way out if you don't want to use the F.W.  And to use the F.>, be sure it's all the way in.  To make the control even more positive, get a steel control lever from an old 2-stroke to replace the nylon one.

Question: I've tested Slick 50 and Moly 2 (molydbenum disulfide).  The Slick 50 is great stuff for the  99.  If you have a 99 and you're ashamed to back it out on the road with anyone listening, give it a treatment of Slick 50.  I did it with one about four years ago for a relative, and I have not had any problem with that gearbox.

Moly 2 is a hardener that they used originally in making steel.  It coats the surfaces by a pressure technique in the 96 gearboxes.  But you don't want to put in too much.  I think the recommended amount for a 96 is two ounces.

Question: Is the gear ratio for a 2-stroke different from a V-4?

Yes.  If you want to have a lot of fun with a vehicle for autocrossing, put a 2-stroke trans in it.  Man, you'll have stump-pulling power, and you can damn near make it fry rubber in third gear.  Everyone will say, "Where in the hell did he get that?" And it's great because you never need fourth gear in an autocross anyway.  I did it for my son in hillclimb.  In Chimney Rock hillclimb, it took seven seconds off of his time.

Question: Some people say not to bother with old "smooth case" 96 transmissions.  How do you feel about that?

I have never seen a case of failure that I could trace to the smooth case itself.

Question: If you've got a spare 96 trans, how do you tell if it's any good before putting it in the car?

When you drain the oil and when you pull the bell housing, if

AN430

you see a lot of debris in either, it will tell you if it's bad or not.  Pull the bell housing and take a look at your primary gear, which is the gear that sits up at the top where your freewheel is.  Look inside the teeth in it.  See if the teeth are chewed up.  The means the F.W. gear has been kickin' that gear.  It it's very bad, then you should consider a check, (diagnostic tear-down).  You can take the top cover plate off and see quite a bit without taking too much apart.

In closing, I'd like to list a few simple truths I know about SAAB 93, 95, 96 and 97 transmissions:

1.Saab factory furnished literature is the ONLY BIBLE on all questions concerning their cars.  NOT Dealer personnel! Certainly not the nice kid who pumps gas at the local Shell stations.

2.Correct gear lube insures correct lubrication.

3.Ball bearings need very little oil, but the supply must be correct and constant.

4.Too great a quantity also raises temperature due to added friction.

5.Clean oil prevents wear.  Change your gear lube every year.

6.A Saab gear lube dipstick, p/n 7862444 is an inexpensive jewel.  Order one through your dealer.

AN430

Specifications, 96 family Gearboxes

Function93-9595-96750GT850GTSonett IISonett

by unit2-stoke2-strokeMonte2-strokeV4-III

3-speed4-speedCarlo

# of teeth 7/38 7/38 7/36 8/39 8/39 9/42

pin/ring

Final Dr5.43:14.88:1 5.14:1 4.67:1 4.67:14.66:1

Gear Ratios

1st gear17.2:119.3:118.3:118.3:118.3:116.2:1

2nd gear 8.5:111.4:110.7:111.4:111.4:1 9.7:1

3rd gear 5.2:1 7.0:1 6.6:1 6.6:1 6.6:1 6.0:1

4th gear NA 4.6:1 4.3:1 4.3:1 4.3:1 3.9:1

Road speed in MPH per 1000 RPM

1st gear 4.1 3.7 4.2 4.2 4.2 4.3

2nd gear 8.4 7.1 6.9 6.9 6.9 7.3

3rd gear11.511.210.410.210.211.9

4th gear NA17.716.117.117.718.2

Specifications, 96 family Gearboxes

Function95/96

by unit V4

# of teeth 8/39

pin/ring

Final Dr4.88:1

Gear Ratios

1st gear17.0:1

2nd gear10.2:1

3rd gear 6.3:1

4th gear 4.4:1

Road speed in MPH per 1000 RPM

1st gear 4.2

2nd gear 6.9

3rd gear11.2

4th gear17.2