AN433

HISTORY OF THE 3 CYLINDER TWO STROKE

Surprisingly, a two stroke engine for the 93 was not a sure bet.  High level talks were held with other manufacturers about co-designing and co-producing a suitable engine.  When this proved unworkable, Saab's manufacturing experience with two strokes, the engine's small size and high specific output must have won the day.  Occasionally it is said that the Saab engine was a copy of an admittedly similar DKW unit.  The connection is through a consultant, who had worked at DKW, that Saab hired to help develop this new engine.

The most commonly asked question about the Saab three-cylinder engine is, why three cylinders?  A full answer is both too long and too technical but let's have a go at a simple, albeit not exactly correct, explanation.

For various engineering reasons, two-cylinder two stroke engines, like that of the 92, produce very little torque and that, over a very narrow rev. range.  This design also has very poor fuel economy when driven hard.  These problems, of torque and fuel deficiency, are in large part due to the basic operating nature of two stroke engines.  That is, when the cylinder is being recharged, both the intake and the exhaust ports are uncovered and this allows some of the new mixture to escape with the outgoing exhaust gas.

The three-cylinder allows a really nifty engineering concept called "pulse charging" to work conveniently.  Conveniently is the key thought as this concept is not limited to three-cylinder engines.  With the help of some fancy math and a suitable manifold, this is how "pulse charging" works.  The exhaust pulse pressure wave from another cylinder arrives to effectively 'seal' the exhaust port of a charging cylinder and thus keeps the incoming fresh charge from escaping.  This greatly increased the engine's efficiency and also 'tunes' the engine for more torque over a much broader rev. range.  For those of you who wish a full explanation, try Chatterton's book, pages 24-25.

It might seem strange that the new three-cylinder engine actually had a smaller displacement than the two cylinder engine it was replacing (748 vs 764).  This new engine size made the competition-minded very happy because it put Saab in the 750cc International racing class.

There was more good news: the power output went up five horsepower to 38bhp (SAE, with an even bigger increase in torque from 41 to 52 ft. lb.  Things were poppin'!

AN433

The 92 had been cooled by what is technically called  thermosiphon. As the coolant is heated by the engine it ruses up to the radiator, is cooled and falls back down to the bottom of the engine to be heated again.  this is how Henry cooled the Model T, but the 93 needed something more sophisticated.  The answer was a modern cooling system  with only a couple of strange twists.  One was that the water pump was made in a unit with the generator.  Why? Sorry, no idea.  The new front design allowed more air through the engine compartment so the radiator blind was moved to behind the front grill.  To allow the warm air to escape, circular holes were added on the wheel arches.  To the very end of this body series in 1980, these vents (made unnecessary and thus filled in during the 1965 changes) could be seen as a reminder of the 93 heritage.  In the 92, the rad provided the heat for the cabin but the cooling system modernization provided the fresh air system with its own separate heat exchanger.  Oh such progress!

This engine was soon hopped up and the first of the special Saabs was on it way.