AN440

CLEANING STROKER EXHAUST

My old two-stroker (Sonett II #187) was losing what little torque an 850 cc 3-cylinder SAAB ever had, so I figured it was time to clean out the exhaust again.

I had done this twice before in two different ways. The first method I had tried had been to take it to the local Redi-Strip place in suburban Chicago and then soak all the bits in their caustic solution. Redi-Strip dunks whole cars to remove the paint without damaging the metal since their solution is caustic not acid. This had worked fine, but there is no such stripping place here in Colorado Springs, so the next time I tried burning it out with my welding torch. This was spectacular as well as effective. I sent the flame up inside the removed parts and as they began to glow red I shut off the acetylene and fed in pure oxygen. Pillars or flame eight feet long and billows of black smoke shot as the oil residues were carbonized. I shook out the ashes and put it back on the car. It ran fine but I realized this was not the safest or most neighborly form of car repair.

This time I decided I would dismantle the resonators and take them to the local auto machine shop to put in their hot tank. The concaved end caps of the resonators are welded to the main tube only at the very end. By cutting just through the tube walls just inside the welds, the caps can be taken off without damage to the parts. Alternating the welds can be ground away. To remove the inlet pipe and tapered cone from the front resonator there are two spot welds part way down the pipe which also must be ground off. These hold the walls of the resonator tube. This creates two holes which must be patched later. By careful working both front and rear resonators can be disassembled.

There should be some fiberglass packing in both front and rear resonators held in place by perforated metal sheet screws. This has long since blown out of the rear resonator, and was intentionally removed from the front resonator. This should probably be removed and replaced if you want optimum performance and no noise. I have upgraded my exhaust to SAAB's rally tune so I've discarded the fiberglass entirely.

I also sawed my double tail pipes into three pieces about three foot long so they could fit into the hot tank. After the visit to the hot tank, the machine shop sandblasted the parts to remove the remaining carbon. The freshly cleaned parts are shown in the picture ready for reassembly.

Eagled eye strokers will notice the modified inlet pipe and the tapered cone for the front resonator. This is as specified by the

AN440

SAAB Stage 3 rally tuning, with the cone moved closer to the inlet by several inches. The internal screens in front resonator are also removed,as are the perforated section of the outlet pipes. This main pipe is also replaced with a section of truck exhaust of the same diameter due to an unfortunate incident with some road debris.

Those who realize that SAAB isn't the only manufacturer of finicky cars that always need tuning will also notice why it is that I've taken two years to get around to writing this article. Three cylinders and no cams are a lot less parts than six with two overhead.

The rewelding is an easy job, except that the front should be tacked welded together in the car to make sure it all lines up right. I left the tail pipe in three sections and made some sleeves out of sheet metal for the joints. All joints are done with the old style sheet metal clamps since these do not crush the tubing. I was very pleased to be able to buy a bundle of these at the 1990 convention.

The car runs great again, and it is all easy to do over when needed. I figured I should be able to cut and reweld 10-20 times before I run out of cutting space. At once every three years, I figure the exhaust will out last me.

I'm still beating my Sonett up on the local autocross circuit, but it is hard to stay competitive against GTI VW's, Acuras and Turbo Isuzus. I recently put a tow bar mount and we have been towing the SAAB to street autocrosses on the other side of the state with Carol Anne's 1973 Volvo wagon (over 11,000 foot passes). The SAAB can make it on its own, but it gets cramped when you squeeze in the tool box, camping gear, four 195/60-15 001 Yokohama tires and two people.

The Sonett is a great ice racer, set FTD every time I take it to local icecrosses. Does pretty well on dirt autocrosses as well. Soon I'll build me a 940cc motor, put in a roll cage and go vintage racing. The old SAAB was meant to race.