AN442

CHANGE V4 VALVE SEALS--IN THE CAR!

The V4 engine can benefit from a valve seal change after about 30,000 miles, or even more often on an engine modified for higher performance.  The reason is that the old umbrella valve stem seals get brittle, crack, or even break up with age.  Exit any sealing for that valve.  These seals CAN be changed IN THE CAR, without removing the cylinder heads.  Shown are the required tools, and the setup being used to change the valve stem seal on the intake valve for no. 4 cylinder.

The KEY to making this tool setup work is pressurizing the cylinder you are working on with air.  Your 1-3 HP roll-around home shop air compressor, if it will produce 90 psi or so, will do the job just fine.  You need an adaptor to screw into the spark plug hole (see sketch) and it's easy to make one up.

Each cylinder must be at TopDeadCentre as you pressurize it.  Then the valves are both closed and the piston at the top of its stroke.  Put the car in gear so the engine can't turn over (or it WILL, as soon as you apply 90 psi of air pressure!), remove the valve cover, the rocker arm assembly and the push rods.  Install the dummy rocker shaft (any old V4 assembly without the rocker arms will do), set the adaptor on top of the valve assembly, hoop up the J-hook tool, depress the valve spring, and use a pencil magnet to retrieve the split key keepers.  Lift off the retained and the valve spring.  Remove the old valve stem seal.  Clean up the area, install a new umbrella seal, replace the valve spring and retainer, depress the spring again with the tool and adaptor, and install the split keys.  Release the depressed valve spring--gently--and go on to the other valve.  Check to see that the split keys seat evenly.

Now you can go on to the next cylinder.  I suggest you start at cylinder 1 and do the job in firing order (1-3-4-2).  Remove the

AN442

air pressure.  I the plugs are out, you should be able to turn the engine over by hand, using the engine fan.  Look at your timing marks.  They will line up for cylinders 1 and 4, and the pulley mark will be on the bottom, 180 degrees away, for cylinders 2 and 3.

Once all 8 seals are replaced, reassemble the push rods and rocker arms, retorque (32 Ft/Lb) the rocker stand bolts, readjust the valves (.014" intake, .016" exhaust), reassemble the rest, and you are done!