AN456

Oil Relay Light Problem

Question:  The cars red oil pressure light comes on with random frequency and duration. It comes on within a mile after it is started cold. Tests on the relay that turns the light on feels that the relay might be bad. The engine was recently overhauled by B&J imports and the car has not been driven very much since the engine was reinstalled. Is there a way of replacing the relay which is no longer available from SAAB.

There is a fix for this warning light syndrome, but let's take a look at how it this thing works in the first place. The schematic shows how the relay is connected and how it is wired internally (disregard for the moment the dashed lines and the second opinion light). On page two is circuit diagram of an exploded view of the actual contact inside the oil pump on the side of the engine. As the pump turns (one revolution for 200 revolutions of the engine) it builds pressure and the piston is raised, pushing the contact sleeve up against the spring and breaking the contact of the contact sleeve with the body of the pump. Until the oil pressure builds sufficiently to compress the spring, current flows from fuse 5 of the fuse box via red wire 111 to the relay box. Inside the relay, current flows and begins to heat the bi-metal strips. The oil warning light will remain on until the spring is compressed in the pump and current stops flowing thru the system.

AN456

2

The relay box has a certain preset delay and must receive a certain number of pulses from the pump before the warning light goes out after staring the engine. According to SAAB, this can take from about 9 seconds up to a minute, depending on the how the car is driven (slow engine speed around town takes longer than running at 60 mph on the highway, etc). Also according to SAAB, the light may flicker if the engine runs at idle for a long time, but it should go out after the engine is run at higher speed for a while.

Current flowing thru the red wire 111 passes thru the windings of the relay and out wire 113 gray to the oil pressure warning light, thru the light to ground. The light lights. This condition will persist until

1) the oil pump has open and closed its electrical contacts enough to shut off current flowing thru yellow wire 112e and 112, or

2) the top bi-metal strip is hot enough to open its contacts, then cools a bit and closes the contacts, then heats up and open its contact, etc. Under these circumstances, the light will flicker.

SAAB goes on to say that the function of the oil warning system is to some extent dependent upon the viscosity of the oil used in the tank, and that in some cars the oil light may wink despite satisfactory lubrication of the engine. As a rule, the reason behind such behavior is that the self-mixing oil with relatively large dilution has been used.

One note about the second light. I used the SAAB warning light, as shown in the drawing. It is a plastic case and you can mount it anywhere. Use a standard 2 watt miniature instrument bulb. If you use any other type of lamp holder, it must be plastic and the type that will not ground out if you mount it to metal, such as the instrument panel. Use the wrong type and you'll either blow fuse 5 or the light will burn all the time, depending on how you wire it. Best to use the SAAB bulb holder if you can.

This is a goofy little circuit that not even the Swedes were very sure about. We think a second opinion is a good idea and the drawing shows how to hook it up (See the dashed lines). Merely add a wire from terminal P of the relay to a warning light similar to the high beam light on the 96, then a wire from that light to the connection on the fan switch with the white wire connected to it, wire 20.

AN456

With this new idiot light, you see a red (or whatever color you use) light until the pump gets the oil pressure up. Then the light goes out. If your stock light comes on, a quick glance at the second (the new one) oil lack of oil pressure is for real.

Why not just replace the old system with the new one, then? Well, I guess because I like two opinions and the old system provides some general information that you don't get with the new. The old system can give you some viscosity clues that the new one won't. I suggest you leave the old system connected, but use the new one as just what I call it --a second opinion. If after initial oil pressure up, the old system shows a red light, have a quick look at the new. If it is not on, probably there is no problem-- you are experiencing a vagary of the old system. But if both lights are on, it's time to shut'er down and find out what is wrong.