AN458

TOW IT RIGHT

I seem to tow a lot of SAABs these days, particularly Sonett's, and I like to make sure they are still behind me when I get home. A solid hitch on the tow car, a good set of towing lights, and a sturdy safety chain are essential, but the heart of the operation is an easy-to-install tow bar mount.

Mine is just wider than the Sonett frame so it slips right up under the car snugly. On Sonett III's I put the front bolt right through the tie down eyes just below the radiator on the frame. Then I push the mount up into place at the back and block it, then drill three 5/6" holes thru the frame on each side, using the mount as a guide. I put in the bolts, nuts washer and tighten and that part is done.

1

I bolt in the tow bar, using 1/2" grade 8 bolts and appropriate spacer washers and snug them down so the bar still pivots easily, then double nut them for security. After hooking up the towing lights and the safety chain, it's time to check over the car to be towed.

I disconnect the battery so I can turn on the ignition to unlock the steering. I make sure the car is out of gear and that the emergency brake is off. I jack up each wheel and check for dragging brakes, loose center hub nuts or missing retainer keys. I inspect the tires for previous unseen damage. I also check under the car for anything loose or hanging down, such as exhaust pipes or a broken rear suspension strap. I check for anything loose in the engine bay and check the fluid level of the transaxle. Finally, I clean the front and rear windshield inside and out so I can see thru the car when I'm towing it.

I tow the car around the block--slowly and with my window down so

AN458

2

I can hear any strange noises and listen to it. If this all goes well, I can be off for home with my latest Sonett.

Towing is not a dangerous activity but one that should be given extra care and caution. There are some DOs and DON'Ts to observe, for your towing pleasure:

DO check your equipment AND the car to be towed very carefully. Be sure the spare is usable.

DO keep your speed down. Observe towing speed limits.

DO downshift for hills--for extra braking power going up extra braking coming down. Take it easy.

DON"T use a turbocharger

car for towing a tow car. You can do grave damage to the turbo, the engine or both. Your turbo engine can only stay on boost for a reasonably short period of time, check your owners manual.

DON"T get in a hurry. Either when you are getting ready to hook up and go, or on the road. When in doubt check everything one more time. You will find it is time well spent. Good towing.