AN46

CHASSIS REINFORCEMENT FOR SONETTS

If your Sonett doesn't handle like it once did, and there is no obvious cause, such as wheel alignment, shocks or tires, there is a good chance it is caused by flexing of the chassis between the front suspension and the firewall. This is especially true as age and rust take their toll.

One method to correct this is to have a plate (3/4")made and attach it to the firewall (weld the bottom and sides but the top should be bolted because of the relative location of the fiberglass body). Weld a 1" X 1" angle iron horizontal to this plate. Taking another 1" angle make the necessary cuts to the ends of this angle and weld it up to the top of the front coil tower. The frame and front end must be aligned before welding.