AN461

TROLLTECH - DISTRIBUTOR/SPARK PLUGS

Question:: How come my '63 850 Normal (as opposed to GT) fouls plugs and runs like it has 1.875 cylinders most of the time, even though it has new plugs, points, condensor, rotor, distributor cap, spark plug wires and complete new exhaust system? Basic static ignition timing is set to 7 degrees BTDC as per SAAB spec. Also the car smokes like hell though I use 1 quart of 40 wt oil for 8 gallons of gas.

There are several things to check:

1. Compression, after the engine had been run enough to warm up. Compression reading should be about 125 psi per cylinder, but the most important thing is that all should be even, assuming they aren't even at, say, 75 psi.

2. Carburetor, the car is smoking a lot, so check the carburetor. It sounds like the mixture is overly fat (rich--ed). Check first the brass float. It may have a hole in it and have sunk, allowing the fuel level to be right to the top of the carburetor, flooding everything. Then check the air jet, which tends to back off of its seat. Then check all the other jets, all of which may or may not be loose in their seats.

3. Spark Plugs, you may want to switch to Champion D6 spark plugs, which tend to run and not foul a bit better in the two-stroke Normal engines.

4. Exhaust System, if all of these things are OK, check the exhaust system, which may be the culprit even if it is new. You may want to modify the front resonator for twin pipe outlets, run a second exhaust pipe parallel to the first and tap into the rear muffler at the front for an inlet for the second exhaust pipe. You would, in effect be making an 850 GT exhaust system and the car will run

AN461

worlds better with that change.

5. Distributor, finally, you should consider locking out the mechanical advance of the distributor is you have a distributor with vacuum advance. The total advantage of the mechanical system plus the vacuum advance system is a bit much for this engine. If it is not right you can have detonation and put a hole in one or more of the pistons, partially because of a questionable exhaust system and partially because of the crappy gas we get these days. A Taurus has knock sensors that retard the advance if you get a batch of bad gas at the station. The SAAB two-stroke doesn't have that sort of technology. Be smart and use premium fuel and lock out that mechanical advance. Set your initial timing to 12 degrees BTDC

instead of the & degrees. The engine you save could be your own!