AN5

SONETT MASTER REBUILD-ALTERNATIVE

When your clutch master cylinder in your Sonett begins to leak fluid, it is of course time to rebuild it before it lets you down on the road/and or your carpeting becomes saturated and ruined.

In most cars, there is no need to remove the cylinder for re-sealing (an unpleasant task) unless extensive corrosion or scoring of the cylinder bore is present. All that need be done is to pick up the carpeting and fold it over to the right side of the vehicle and out of the way, thereby exposing the pedal cover plates. With the help of a light, verify that there is fluid leaking on and around the rubber dust cap, clutch pushrod and probably the floor by now, too.

Once this leakage has been verified, open the bleeding screw at the slave cylinder and purge all of the fluid in the reservoir by repeatedly depressing the pedal, This will reduce the amount of fluid that will escape from the master cylinder when the piston assembly is removed.

Remove the clutch pedal cover plate, and place a few rags beneath the master cylinder to catch and absorb the small amount of fluid that runs out.

Peel back the dust cover (No 11) and using a pair of long nose pliers remove the lock ring (13). Also remove the clevis pin that attaches the pushrod to the clutch pedal: the pushrod (12) can now be removed. This will expose the piston, and a magnet may be helpful in getting the piston out far enough to grasp it for removal.

At this time the cylinder should be swabbed out with alcohol or brakleen, and the bore inspected for serviceability. If only minor scoring is present the rebuild should be successful.

Disassembly is per the illustration shows, and in the Girling rebuild kit, P/N 78-46-082 and assembly is simply the reverse.

This job can be done thoroughly in less than an hour, with one tenth the aggravation of removal from the car, and long time Sonett owners are probably aware of this technique, so I feel everyone should have this as an option come rebuild time.