AN51

MANUAL CHOKE CONVERSION, SAAB V-4

SOLEX 28-32 PDSIT-7

1. Disassemble the automatic choke. Block off the small water hoses to the choke.

2. Discard water manifold and bolt. Pry open spring clamp and remove the bimetal spring.

3. Drill a 5/16" hole through spring body.

4. Use a parting stone and cut down the inner section about 1/4" so bolt will clear choke mechanism.

5. Use a 5/16" SAE bolt about 1-3/4" long, weld a tab on the bolt head and slot the tab with a hacksaw and file. Assemble as below. Mount on the carb so tab engages the choke lever and so cable arm doesn't hit distributor.

6. Operation- You'll have to depress the throttle slightly to pull the choke "ON". Throttle fast idle will engage (and adjust) as before. Use a universal choke cable. Clamp cable body to left valve cover plug wire.

Note it will be easy to over choke (and flood) the engine so experiment a bit to get it right.