AN59

HEATER VALVE CONTROL REPLACEMENT

As cars age strange parts finally fail. This one is quite expensive from SAAB, but a good quality replacement is available from Ford for a quarter of the price. Ford P/N BBC-18495-A. Mount to the tubular SAAB engine bay brace.

Mount the valve with 2 (1/4") bolts, nuts and lockwashers. The stock SAAB control cable will reach if you mount the valve on the engine bay cross brace. Some household copper pipe bent at 90 degrees, a short length of heater hose plus some hose clamps will make the necessary connections.

Remove the old valve or just leave it in the car. If completed properly the control valve in the car will work just as before.