AN6

SONETT WATERPUMP, SANKO AIR CONDITIONER

WATERPUMP: J.C. Whitney is still a bargain for the pump. I did not find it necessary to remove the motor mount in order to get at the inside bolts as it was suggested in a recent newsletter. A 10 mm socket with a short extension on a 1/4" ratchet will do the job very well. The 1/4" ratchet is so short that there is plenty of maneuvering room; there was none with my 3/8" ratchet, although I did manage to get one of the bolts with a universal joint and a long extension before I discovered the 1/4" approach. I replaced all the hoses while I had the system open: 4 inches of 1" hose going straight back, flex hose at top and bottom of the radiator, and standard 5/8 inch hose most everywhere else. I sprayed all the hoses with Armorall before installing.

According to the manufacture, Sonett water pump is identical to 1969-71 Capri 1300,1500,1700.

ENGINE FRONT COVER: I could have saved all the time in removing the water pump, since I later decided that new gaskets on the front cover and intermediate plate might help the chronic oil leak at the front of the engine. (It might also be due to the Arco graphite oil I was using, since it was never this bad before.) The gaskets are cheap and the job is real easy, although the seal for the balance shaft cost about $10.00, and should be replaced at the same time. The water pump goes off and on very easily once the front cover is off. I chipped the balance shaft pulley when taking it off and was very fortunate to find a used one at the local dealer at a reasonable price. The double pulley in air-conditioned Sonetts is not a standard SAAB part. The Haynes manual for the V-4 contains good directions for removing and replacing the front cover and the intermediate plate, except that it fails to note that you chew up part of the oil pan gasket in the process. It later points out that you have to pull the engine to remove the oil pan and replace the gasket. Not wishing to do this, I bought a new oil pan gasket, cut off the part that sits under the front cover, and used liberal quantities of silicone gasket sealer at the corners.

REMOVAL OF THE HOOD: I could never remove or replace the hood without some choice words for the guy who designed the headlight linkage. (You could correctly point out that it is really the fault of the guy who put the air conditioner there. Regardless, it was a dirty, knuckle busting job.) The two bolts are hard to get at due to the air conditioner. The nuts are not accessible from the inside of the engine compartment for the same reason. And the whole thing is located in the greasiest corner of the engine, making it generally an unpleasant job. I always needed a helper to keep the nuts from spinning, since I couldn't reach both ends at the same time. I wrote you last year with some thoughts on how I might solve this problem. and this summer I did it. I took care of the stationary arm with a pseudo-captive nut which I made by brazing a 1/4-20 nut aver a hole in a piece of 3/4 X 1-1/2 inch steel. If I had the right tap and drill, I could have just made a threaded hole in the piece of steel. I can easily hold this in position with my fingers while I start the bolt; once the bolt is started the steel strip keeps the nut from turning. I substituted a clevis pin for the nut and bolt that pinned one I could get at the hardware store was 1/2" by about 2" with holes every 1/8" I cut it down to about 1-1/8" rounded the corners, and drilled out the hole in the control arm yoke to 1/4". I inserted it from the engine compartment side, them secure it from the outside with a washer and a hitch pin clip (from hardware store-- looks like a large bobby pin). If the hitch pin clip were an the inside, it would come a little too close to the air conditioner pulley. I plan to check periodically for wear on the clevis pin, since this approach eliminates the sleeve which surrounded the original bolt and protected it from wear, but I don't really think it will be much of a problem. The whole job now takes just a couple of minutes and only requires one person.

SANKYO ROTARY AIR CONDITIONER: I ordered this from Time Machines in Brooklyn. They drop ship direct from Clardy in Texas, which appears to be the importer. Service was very fast. Time Machines ordered a unit with a 5" pulley instead of the 6" pulley that the original York unit had, but the technical staff at Clardy assured me that this was fine, and probably even a bit better for city traffic. the unit fits easily in the Sonett and takes up less useful space that the York. The major problem is that the fuel pump interferes with the necessary mounting bracket and must be removed. I switched to an electric fuel pump a year ago, so it was just a matter of cutting a plate to the shape of the fuel pump gasket and mounting the plate and gasket where the pump was. I had to put a couple of washers under each of the mounting bolts to make up for the thickness of the base of the pump, since the bolts bottomed out without them. I recommend an electric fuel pump for any Sonett with air conditioning. The mechanical pump is almost inaccessible, its filter cannot be removed for cleaning, its location right behind the radiator and near the exhaust pipe is conducive to vapor lock, and the right angle bend the output line has to make can crimp the line and shut off the gas. I haven't yet completed installation of the Sankyo. It will require right angle flare fittings to connect the existing hoses, and will perhaps need an extension to the existing hose on the high pressure side. I haven't checked the belt length yet.