AN66

TRANSMISSION ALIGNMENT V-4

When putting the V-4 and transaxle back into the 95/96/97, I used to constantly fight with the drive train trying to fit the transaxle into the back mount.

Then I came up with the idea that speed up the process 10 fold.

Before you lower the engine/transaxle into the engine compartment, slip a line up tool or a pin punch into the threaded hole at the back of the transaxle. This method does an excellent job of lining everything up. After everything is in place, simply pull the punch out and install the bolt.