AN74R

TRANSMISSION FREEING FROM REAR MOUNT

1

The drawing shows a neat trick for removing 95/96/ & 97 gearboxes when the gearbox is stuck in the rear mount. Most people try prying against the box with a crow bar and using the engine cross bay brace member for leverage. All that happens, however is that you bend the cross brace and possibly knock a hole in the top cover of the gear box. If you look at the firewall with carpet and padding removed you'll see a smaller rubber plug just above the large plug that gives access to the bolt. Remove the small plug and using a drift or other similar tool, hit the bottom of the mount a couple good wacks while a helper pulls on the gear box from the front. It works surprisingly well and will save an hour of prying and cursing. To make things easier the next time, smear the inside of the mount with anti-seize. When the transmission is out is also a good time to check the condition of the rear mount and change it if the rubber looks suspect. It'll save pulling the engine latter.