AN81

V-4 CARB CONVERSION TO MSS & SOLEX

I tried a 43mm barrel Motorsport carb on my '71 95 last winter and spring and based on that experience I do not recommend it. Power was if at all only slightly improved, gas mileage stayed the same, the manual choke proved difficult to adjust , installation was not simple (ie. no provision for fuel evaporative canister purge hose, other problems). This carb requires that the PVC system be blocked off which in one emission control device I approve of, and is not cheap, requiring one of Motorsport's modified intake manifolds. I would be interested to hear from people that had good luck with one of these carbs.

I have had increasingly bad luck converting Autolite V-4 carbs to Solex's. After a few successes (a '69 95 in particular that gets 30+ MPG consistently even though it has over 210,000 miles on an original engine) I'm finding good Solexes hard to come by and now will only do the conversion to '69 and '70's (the years with the worst Autolites) only if I cannot find a later model Autolite. Following the choke and other adjustments carefully in the Haynes manual, it is possible to get a very good running car from the '71 and '72 TF and TW9510 carbs.

When converting to a Solex I have found the best jet sizes to be 127.5 main, 110 emulsion, and 42.5 idle at my altitude 5,000 feet. I use a 1967/68 accelerator linkage shaft (P/N 88-00-542) with about 1-1/4" cut off of the heater box end and a 1967/68 shaft to carb link (P/N 88-00-559) to make up the linkage.

I have also noticed a very strange thing happening to the timing on most of my Solex equipped cars. When throttle is opened, the timing initially RETARDS about 3 degrees before advancing. Timing does not advance any more than it would without the vacuum hose attached; in other words, it appears that with the vacuum hose CONNECTED, timing is at first retarded then has no further effect on the advance. I have seen enough of these cars to suspect a problem of compatibility between the Solex carb vacuum advance porting/strength, and the later model distributor vacuum advance diaphragm, as this is mostly happening on cars that I have converted from Autolite to Solex, although it is happening on at least one car ('67) with original specifications. The solution has been to disconnect and plug the vacuum lines from the carb, eliminating the stumble on acceleration present before the disconnect.