AN86

GOOD RESULTS WITH MSS CARB

Response to complaints on the 43mm one barrell carburetor and intake manifold as purchased from MSS.

I have had the above system on my '69 96 for over 40,000 miles. I keep careful records on gas mileage and regularly time my engine's performance by checking acceleration from 40-60 mph in third gear, and 50-70 in 4th gear. The carb and manifold do improve power and acceleration, however slightly. It might be that Mr. Killinger did not experience this boost because he was using a stock exhaust system. I have the extractor exhaust that is also sold by MSS, and the addition of this undoubtedly enhances the effect of the new carb. Acceleration times were improved by .4 seconds from 40-60 and almost 2 seconds from 50-70 in 4th gear. So the power is there. I carefully check the gas mileage before and after installation, and the carb system is good for about 1.5 mpg improvement in overall driving.

I've put over 80,000 miles on the 96, and it has proven to be durable and trouble free. No transmission work has been need in 140,000 and it's only required one clutch/pressure plate change, minimal brake work, with only two clutch slave cylinder rebuilds, one valve job at 50,000 miles. Little by little I've made changes to improve gas mileage:

: Bilstien shocks in front to keep the front end on the road.

: Allison photo-electric ignition and silicone ignition wires.

: 43mm carb and intake manifold from MSS.

: The use of Key Oil in the engine (+3 mpg alone).

: The use of Moly in the 75 wt. transmission oil.

: Modified the air cleaner according to SAAB rally specs.

: Steel belted Michelin radials.

: Careful adjustment of rear brakes (no dragging)

: NGK spark plugs

With all of the above, the gas mileage at 55 was a steady 36 to 38 mpg. But then I installed the SAAB front spoiler. The spoiler did more than anything for gas mileage and even accomplished what the SAAB people said it would, increase handling stability and cut wind and road noise. The spoiler was worth a good 8% increase in gas mileage. On a trip to Nebraska last summer I netted an average of 39.4 mpg, which included a few trips around town while visiting. The two highest mpg figures I got were 40.8 and 41.4 and that's after deducting the 3% for error off the odometer reading.