AN9

SONETT III REAR HATCH BUTTON

In the newsletter for Nov/Dec '78, I read with interest (page 6) about a modification of the plastic button on the Sonett's rear hatch. I've had a lot of trouble with that thing--seems to me the basic design leaves something to be desired, so I had a permanent replacement made which is far superior to the original. I went to a machinist friend and had him fabricate one out of steel.

The base is no longer than that of the stock button, giving more threads in the base than in the original for a positive engagement with the threaded plunger. I made a washer from 3/32" rubber gasket material to go between the head of the button and the hatch for a weather seal. I wrapped the base with plastic tape to isolate it from the glass hole.

My button is ordinary steel and requires a coat of primer and some black enamel as a rust preventative; you could easily make it out of SST and eliminate the painting and rusting problems.