AN95

WATER INJECTION

Water injection works great on the V-4, it will eliminate the need to buy premium gas.

There are many units available but I like the one made by Shelby-Spearco. It is advertised in the auto magazines and also J.C. Whitney. It is an expensive unit compared to others I have seen but it has some real advantages if you are interesting in doing things right. The Shelby unit can be adjusted to start at various settings and uses an electronic unit to vary the rpm of the injector (windshield washer) motor. More rpm more water. Also there is the possibility of various jets to control the maximum flow.

I put one of these on my 95 and the detonation went away. I also have been using one on my turbo V-4 for about a year now with no problems. I mix 50-50 methanol to avoid freeze up in cold weather and a splash of methanol in the summer for fun. the jets that come with the kit are a bit large for the V-4 so I tapped the hole shut with a hammer and redrilled them. I also installed a filter in the line as the jet could easily become plugged.

There are more basic units that consist of a vacuum switch and pump only that work well, but lack the proportional flow adjustment of the Shelby-Spearco.