AN97

CARB MSS

Jack Lawrence summed up the V-4 carb situation pretty much as I had analyzed it. I think the Weber as once offers by SAAB as part of the Stage i tuning kit might have been slightly better, but lacking that kit, the expense along with the linkage and air cleaner problems, especially in a Sonett, made me decide on the 43mm MSS carb.

I installed the carb last fall and am pleased, although I did not get much use before I put the car up for the winter. My mpg went up about 1.5 mpg. The beauty of the MSS carb is its simplicity. Several troublesome emission controls are eliminated, and there are only two adjustments: idle speed and idle mix. Best idle results in a complete stall when the throttle was just open, making it impossible to ease away from a light. I solved it by adjusting the mix with the idle set for 1500-2000 rpm, then turning the idle down. (Ed. note: I experienced the same problem with my MSS carb, but talking with Jack, he says that the 1500cc V-4 need a different jetting than the 1700cc and that will eliminate this problem. I haven't had a chance to check the jets in my carb yet to try this.)

I experienced a balky choke problem, but found the problem was in the cable. I re-routed it for more generous bends and put graphite speedometer grease on the inside, and the problem wa solved. I plan to re-contour the fast idle cam next spring. The 43mm is a Holley designed for Ford product with a larger engine, and you get too much fast idle for a small engine unless you back the screw all the way back. Then you get no fast idle until the choke is all the way out.

Changing the manifold on a V-4 engine is compared to changing the head on an inline four. That is, you break into both the water and oil passages and can mix the two if you're not careful. BE SURE TO DRAIN THE ANTIFREEZE FROM BOTH BLOCK DRAINS, NOT JUST THE RADIATOR and preferably flush the block with water. A little water won't hurt your oil but antifreeze will.

Before you begin this installation, check your compression. there is no point in putting a big carb on a sick engine. You may need a valve job, and now is the time to do it because you are doing half the labor anyway. if you do a valve job, consider stiffer valve springs. be sure to adjust the valves while you have the valve covers off. Valve failure is the largest single cause of a V-4 engine failure.

Finishing touches: the water lines that went to the old choke should be plugged at both ends. The valve cover vent on the left-hand cover can be returned to the carb inlet by adding a tee to the hose from the carbon canister. The hole on the front of the air cleaner that went to the old float bowl vent should be plugged. notches must be filed inside the air cleaner where it fits over the hold down bail on the carb.