AN98

V-4 OIL PRESSURE SWITCH

V-4 oil pressure sending units often leak and/or stop working. Don't let a bad sending unit cause a blown engine! If the oil pressure idiot light doesn't come on when the ignition is turned on, check the sending unit by removing the wire from the unit and grounding it. If the light now comes on, the sending unit is bad. Trouble could also be in wiring, especially in the connection at the gauge cluster of the 1970 and on V-4's. Parts numbers are Beck-Arnley 201-0064 and Standard PS-57 available from an American parts distributor (designed to fit most GM cars, take old sender to compare).