AN99

CARB CHOKE OPERATION, MANUAL CHOKE

Several contributions now discuss how to change to hand choke, including one by Ashcraft in Jan. '81 issue. All these results in most unsatisfactory choke. Good choke function must include at least so called "draw down", so the choke plate opens further as air flow increases. This is usually accomplished by light spring pressure against unequal arm butterfly. Many also have intake vacuum control on butterfly position. When the butterfly position is simply fixed by a pull wire a degree of choke appropriate, eg at idle will simply flood the engine out when you drive off.

Ed Note: My experience with manual chokers is that to get the desired "draw down" or partial opening of the butterfly plate you push the choke in a hair right after the engine fires and catches. After that you have much more control over the choke position than with the automatic choke. For instance if you have a steady drive with no stops right after starting up, you can shut off the manual choke completely and save gas as well as wear on the engine from excess gas washing oil off of the cylinder walls. With the automatic choke the butterfly plate stays partially closed until the engine warms up to the specified coolant temperature, regardless of the load on the engine or type of driving.