NE 18

AIR CONDITIONING

For those Sonett III owners with A/C, the following is an attempt to answer some questions about parts availability.  A parts book is available from SAAB, PN 02-99-693.  This gives parts lists and part numbers for all the A/C installations for Models 95, 96, 97-Sonett, 99 and 99 Turbo through 1980.

To answer some specifics, the Coil-Condenser, PN 02-62-386, and the Fan Motor, PN 02-62-402, were still in stock as of August.  The Sight Glass w/tap and the Receiver-Drier were not in stock as of the same date.  However, the good news about these two parts is that with a bit of re-piping and the 99 Receiver-Drier w/taps, PN 02-65-207, can be used to replace these items.  The A/C drive belt is SAAB PN 02-64-168 with equivalent US belts as follows:  NAPA 25-11454, Gates 7470 and Dayco 15470.  All the fittings and hoses are US auto A/C parts, available at any automobile A/C shop.  Take the SAAB part with you as a sample to avoid confusion.  The compressor is a US York "Mini 206" or so says the parts book.  I have repaired A/C systems on two Sonett III's with only minor difficulties.