NE19

WALTER'S WORKSHOP

Recently I began noticing occasional miss-firing with my 1974 Sonett III.  I tried several things to determine the cause, to no avail.  Then I looked at the spark plugs and discovered that #1 was fouled with coolant.  I diagnosed a leaking head gasket and finally got this fixed (along with a much needed valve job as it turned out) only to find that it was the intake manifold gasket that was leaking!!  I should have noticed that the cooling system was not being pressurized by the leak and so the head gasket was probably not to blame.

I have just had what may be an unusual failure in a front brake flexible line.  The ling plugged up when I applied the brakes and the caliper did not release.  I thought that the caliper itself was stuck and causing the problem so I drove it some more with the caliper stuck!  Wrong move!  The brake disc got so hot that the grease boiled out so that the wheel bearing was damaged.  I have now been told by Bud Clark that the remedy is to open the wheel brake cylinder bleeder nipple which will release the fluid pressure.  This will determine the real cause of the lock-up.  Replacing the flexible front brake lines would appear to be a good move if the Sonett still had old or dried out lines.

During the work mentioned above, the three vacuum hoses form the thermostat housing to the deceleration valve, the throttle body and the distributor were disconnected and no one in the shop knew what the correct connections should be!  I looked in the ship manual and verified the following connection order with Bud Clark who works on V4 engines all the time.